## Slide 1
Principios de las nuevas tecnologías

## Slide 2: Una perspectiva basada en la terapia del movimiento.
El contenido de esta presentación se basa en la presentación de IISART, revisada, traducida y adaptada por Centro Europeo de Neurociencias.
Puedes utilizar el contenido de esta presentación con tus pacientes y tus compañeros de trabajo, eso si, referencia siempre y en todo momento el origen y los autores de la misma.
Si el contenido de esta presentación va a ser utilizada en cualquier formación, curso, congreso, jornada, etc., se deberá pedir primero permiso a los autores de la misma.

## Slide 3: Audiencia
Clínicos
Investigadores
Ingenieros
Otros
Objetivos de aprendizaje:
Conocer los fundamentos sobre los que se basan las nuevas tecnologías en rehabilitación.
Notes: [Attention: slide contains animations.]
Target audience: Clinicians, engineers and scientists or anyone with an interest in the application of new technologies for neurorehabilitation.
Aim of this slide pool: Provide a concise and comprehensive summary about new technologies in rehabilitation.

## Slide 4: Razones para el uso de nuevas tecnologías
Sociedad
Tecnológico
Clínico
Envejecimiento de la población.
Coste sanitario
Carga en la vida diaria
Tecnología disponible
Rápido crecimiento
Uso en el hogar
Potencial de recuperación sin usar
Conocimiento basado en la evidencia
Notes: There are various reasons why new technologies are becoming more and more applied in rehabilitation. One group of such reasons can be summarized as societal drivers. These include for example the overaging of the population (in 2030 around 25% of people will be over 65; in 2050 this number will have more than doubled), the rising cost of health care and the increasing burden impairments have on daily life.
There is a therefore need for new approaches that can cope with the future demand. New technologies are very likely part of the solution to enable more efficient rehabilitation (higher intensity) which can also take place outside of hospitals. They might also help to lower health care costs and increase the part of recovery which the patients can do by themselves.
Another driving force is the current advanced state of available technology as well as the fast developement of new technologies. This opens up new fields of application and changes the attitude towards the use of new technologies. Nowadays for example technology gets more and more accepted in hospitals and rehabilitation centers. Progress in technology also makes it possible to bring therapy from the hospital into patients’ homes.
A third point that drives the application of new technologies in rehabilitation comes from the clinical side. Current recovery progress for conventional therapy still seems to have room for improvement. In addition, new evidence-based knowledge is continuously gained and pushed new treatment methods.
Historically Rehabilitation has been the poor relation in medicine
Absence of scientific rationale
Absence of evidence
No conventional rehabilitation procedures are any better than any other but intensity is important (Pomeroy)
Recovery of lower limb function (walking) is better than upper limb function (Hiraoka 2001)
Of a sample of patients with no active upper limb movement on admission:
14% experienced complete recovery
30% partial recovery
56 % had no recovery (Hendricks 2002)
5% of survivors with severe paresis regain upper limb function (Barecca 2001)
Can we do better?
For successful clinical use systems must be:
Robust and reliable
Motivating, engaging and easy for patients to use
Made possible by advances in electronic and software design, signal processing and control engineering
Demonstrate clinical benefit and cost-effectiveness
Driven by a better understanding of the neuroscience of motor learning and control

## Slide 5: Utilización de las nuevas tecnologías
Aprendizaje motor
Daño cerebral
Terapia
Valoraciones
Actividades diarias
Nuevas tecnologías para mejorar la eficacia y efectividad de la terapia.
...y valorar el progreso en la recuperación

## Slide 6: Integración de las nuevas tecnologías
Los clínicos diseñan valoraciones y programas de tratamiento usando las tecnologías para mejorar la rehabilitación de los pacientes.

## Slide 7: Potencial influencia de las nuevas tecnologías
Tecnología avanzada en rehabilitación
Repeticiones variadas y orientadas a un objetivo & feedback de ejecución exitosa.
Reduce el apoyo
Incremento del desafío
Input de movimiento y sensitivo
Fuerza muscular
Neuroplasticidad y aprendizaje motor
Mejora de la ejecución
Notes: From a presentation by Jane Burridge:
For normal motor learning to occur, the individual must be able to perform the task – even though performance may be imperfect. With repetition, feedback of performance, motivation, encouragement etc. performance improves. Where motor control is severely limited the individual is unable to perform the task and so cannot practice effectively and often receives negative or absent feedback, they may become discouraged and de-motivated. For an individual who has one normally functioning arm and hand the temptation is strong to perform tasks one handed – with the consequent learnt disuse effect.
By augmenting the individual’s performance using new technologies some of these problems can be overcome

## Slide 8: Contents
Terapia asistida por robots
Sistemas no motorizados
Estimulación eléctrica funcional (FES)
Tecnología de sensores
Realidad virtual
Estimulación cerebral

## Slide 9: Terapia asistida por robots
1

## Slide 10: Robótica en rehabilitación
La idea de utilizer robots en rehabilitación surgió durante la década de los 80.
  Liberar a los terapuetas de un trabajo duro y repetitive.
  Incrementar la consistencia y volume de las repeticiones.
“La robótica en rehabilitación es una rama concreta de la robótica que se centra en máquinas que ayuden a las personas a recuperarse de un trauma físico grave o les asistan en las actividades de la vida diaria.” History and Future of Rehabilitation Robotics, Frumento et al. 2010
Concepto:
Ortesis brazo/pierna
Robot terapeútico
+
=
Robot industrial
Notes: “A robot is a reprogrammable, multifunctional manipulator designed to move material, parts, tools, or specialized devices through variable programmed motions for the performance of a variety of tasks.” (Robot Institute of America)
“Robotics is the science and technology of the design of mechatronic systems capable of generating and controlling motion and force.” Paolo Dario (~2000)
Rehabilitation Robotics has been defined a special branch of robotics which focuses on machines that can be used to help people recover from severe physical trauma or assist them in activities of daily living (History and Future of Rehabilitation Robotics, Frumento et al. 2010).
Design, construction, and use of machines (robots) to perform tasks done traditionally by human beings [Merriam-Webster Dictionaries]
Textbook of Neural Repair and Rehabilitation, Krebs et al., Chapter 48: REHABILITATION ROBOTICS, ORTHOTICS, AND PROSTHETICS
Rehabilitation Robotics encompasses an emerging class of interactive, user-friendly, clinical devices designed to evaluate patients and, also deliver therapy. Robots and computers are being harnessed to support and enhance clinicians’ productivity, thereby facilitating a disabled individual's functional recovery.
Application of robotic technology to the rehabilitation needs of people with disabilities as well as the growing elderly population [Hillman 1998 Robotica]. Developed as an advancement from existing technology .

## Slide 11: Terapia robótica: Elementos
Estructura mecánica
Segmentos y articulaciones movibles
Motores
Convierten la energía en movimiento y fuerza.
Miden parámetros físicos: posición, fuerza, orientación, torsión
Controlador
Utiliza la información del sensor para controlar los motores
Interfaz paciente
Se une al paciente y transmite las fuerzas desde el robot p.e cuffs
Interfaz de usuario
Permite al usuario ajustar los parámetros
Fuente de alimentación
Proporciona electricidad a los motores y controladores
Fuente de alimentación
controlador
motores
sensores
interfaz paciente
interfaz de usuario
Estructura mecánica

## Slide 12: Terapia Robótica: Dispositivos
Localización fijación
Miembros superiores
Miembros inferiores
¿Cómo categorizar los dispositivos robóticos terapeúticos?
Estructura mecánica
Exoesqueletos
Efector final
Estrategias de control
Guía total
Cooperación paciente
Espacio libre

## Slide 13: Terapia robótica: Exoesqueletos
Unido al cuerpo o partes del cuerpo
Las articulaciones transmiten fuerzas a los diferentes sistemas robóticos
Permite la producción de movimientos fisiológicos
Combinación con Cintas de marcha, sistemas de soporte de peso, estimulacion eléctrica functional, realidad virtual.
“Un robot usable o estructuras mecánicas externas con articulaciones y conexiones que se corresponden con el cuerpo humano.”
Pons et al., 2006; History and Future of Rehabilitation Robotics, 2010
Miembro superior
Miembro inferior
Notes: -Generally complex devices with several degrees of freedom (DOF) of several independently driven joints
-Attached to body or body parts
-Actuators generate torques applied on the human joints
-Driving the actuators in well-defined and timed sequences with the exoskeleton aligned to the human joints allows production of physiological movements
-For training locomotion often combined with a body weight support system and a moving treadmill
ROBOTICS IN NEURO-REHABILITATION
Loris Pignolo, Eng 2009
Exoskeletons are robotic manipulators worn by the operator, with links and joints replicating with due approximation those of the human skeleton (Fig. 2). Three main modalities of use are possible: • strength enhancement, when greater load and resistance is required in peculiar conditions and the exoskeleton shares the load;
• haptic functions, when the actuators feedback the operator with sensory information on remote motion or tactile perception;
• motor rehabilitation; in this case, the exoskeleton worn by the subject with disabled upper (or lower) limb compensates for the lack of strength or precision in tasks compatible with the requirements of everyday’s life or profession in a formal training programme.
Device examples:
• MULOS System (Scuola Superiore Sant’Anna, Pisa, Italy, 1994);
• Salford Rehab Exos (Salford University, Salford, UK, 1999);
• ARMin (Swiss Federal Institute of Technology, Zürich, Switzerland, 2006);
• Nagoya University system (Nagoya University, Nagoya, Japan, 2003);
• T-WREX (Machines Assisting Recovery from Stroke (MARS) Rehabilitation Engineering Research Center (RERC) on Rehabilitation Robotics and Telemanipulation, Chicago, IL, USA, 2004);
• WOTAS (Wearable Orthosis for Tremor Assessment and Suppression) (Instituto de Automática Industrial, Madrid, Spain and Hôpital Erasme ULB, Brussels, Belgium, 2006)
Exoskeletons offer greater DOF numbers up to 7 active DOF, with guaranteed optimal control of the arm and wrist movement (Fig. 3). However, also in the event of compact and light systems, the motors necessary to enliven the DOF are often conspicuous and require careful and frequent maintenance. Moreover, these systems are difficult to little transport to the patient’s home and their use is often restricted to research into the kinematics and dynamics of the human body.
Loureiro et al. 2011
Exoskeleton system encapsulate the arm on the mechanism providing the opportunity to control the orientation of the arm where the degrees of freedom are active. The arm’s joint axes are fully determined (allows a larger workspace), joint misalignments are possible when robot axes do not align correctly with the patient’s arm anatomical axes.

## Slide 14
Unido a un solo segment corporal
Transmite la fuerza a través de una cadena de movimiento mecánica.
Combinación con Cintas de marcha, sistemas de soporte de peso, estimulacion eléctrica functional, realidad virtual.
“Sistemas robóticos que proporcionan un soporte y fuerzas a los miembros del paciente pero solo en la parte más distal (efector final) que está unido a la extremidad del paciente.”
Maciejasz et al., 2014
Miembros superiores
Miembros inferiores
Terapia robótica: Sistemas de efector final
Notes: -Technically more simple devices
-Attached to a single body segment through its end effector
-End effector movements change the position of the segment of the limb to which the device is attached
- Creates a mechanical chain in which the movement is transmitted to other segments of the patient’s body
-For training locomotion often combined with a body weight support system and a moving treadmill
ROBOTICS IN NEURO-REHABILITATION
Loris Pignolo, Eng 2009
Operational-type machines restrict the patient/machine interaction at the end-effector level (Fig. 4). The system designs for the end-effector trajectories match the hand’s natural trajectory in space for the required task. As a result, motor exercises in the real world can be programmed easily; the natural synergy between end-effector and distal (upper) limb determines the functional arrangement of the arm. Operational-type machines have been designed for application to neuro-rehabilitation:
• MIT-Manus (Massachusetts Institute of Technology, Cambridge, USA, 1997) (8);
• ARM-Guide (Assisted Rehabilitation and Measure Guide) (Sensory Motor Performance Program, Rehabilitation Institute of Chicago, Chicago, IL, USA, 2000) (33);
• MIME (Rehabilitation Research and Development Center, VA Palo Alto Health Care System, Palo Alto, CA, USA, 1999) (34);
• Bi–Manual rehabilitators (Research and Development Center of Excellence on Mobility, Department o f Veterans Affairs Palo Alto Health Care System, Palo Alto, CA, USA, 2000) (35);
• MEMOS (MEchatronic system for MOtor recovery after Stroke) (ArtsLab, CRIM Scuola Superiore Sant’Anna, Pisa, Italy, 2005) (36);
• BRACCIO DI FERRO (Neurolab-DIST, Università di Genova and Italian Institute of Technology, Genova, Italy, 2006) (37);
• Robotherapist (Osaka University, Osaka, Japan, 2006) (38);
• GENTLE S (Human Robot Interface Laboratory, Department of Cybernetics and School of Systems Engineering, The University of Reading, Whiteknights, Reading, UK, 2003) (39);
• Nerebot – MAribot (Department of Innovation in Mechanics and Management (DIMEG), University of Padua, Italy, 2006) (40);
• Bi- Manu- Track (Reha-Stim, Berlin, Germany, 2005) (41);
• GENTLE System (Human Robot Interface Laboratory, Department of Cybernetics and School of Systems Engineering, The University of Reading, Whiteknights, Reading, UK, 2001) (42).
Loureiro et al. 2011
End-effector systems related to systems that interact with the patient using a single distal attachment point on the forearm by meansof an orthosis. Exercises are defined in the XYZ Cartesian space relative to the robot’s single end-effector attachment point. The single attachment point results in a number of possible shoulder and elbow rotations which could lead to joint injuries when performing unsupported 3D spatial movements. Some systems use a dual robot configuration to address this problem (to different end-effectors attached to two points).

## Slide 15: Exoesqueletos vs. Sistemas efector final
Exoesqueletos
Efector final
  Control y estructura más simple
  Fácil de ajustar al paciente
  La posición del miembro no está completamente determinada
  Información de la fuerza y posición limitada
  Riesgo de lesión de las articulaciones
  Ejes de movimiento completamente determinados
  Movimientos fisiológicos
  Información de fuerza y posición de cada articulación
  Los ejes del robot se tienen que alinear con los ejes anatómicos
  El tiempo para ajustar todo es mayor
  Desafíos por las restricciones anatómicas
Notes: End-effector based
-Simpler structure and algorithms
-Smaller injury risk
-Faster set-up routine
-Less control of movement pattern
-Force and position data of distal parts
-Risk of injury through unphysiological movement
Exoskeleton
-Force and position data of joints
-Individualized resistance
-Physiological movements
-Expensive parts
-Significant device set-up times
-Challenging alignment to anatomical constraints
-Greater possibility of skin irritation
Feedback
Foot plates provide afferent feedback that is different from feedback during normal walking (e.g.loading and foot soles).
Physiologic gait pattern with correct sensory input (dynamic loading, hip extension, foot soles) triggers central pattern generators (Pang et al., 2000; Dietz et al., 2002).
Exoskeleton adjustable to different patients requirements allowing long and challenging training sessions (stabilizes and controls hip and knee movements, adjustable guidance force …)
In severely impaired patients lack of knee and hip control might bare the risk of knee hyperextension  therapist eventually has to guide the knee. A solution is to use an exoskeleton or multiple end-effector robots attached to different end points.
In patients that are already able to perform overground walking End-effector based systems provide more degrees of freedom
Exoskeleton provides ability to assess function (Schmartz et al., 2010; Mirbagheri et al., 2011) or train against resistance (Lam et al., 2011 Houldin et al., 2011)
Robert Riener:
Why Exoskeletons for Arm Therapy
- Better joint control (each actuator drives a joint axis)
- Better cope with singularities of human arm
- Higher safety
- Larger range of motion
- Training of ADL tasks, transfer to daily life
Not only treat impairment, but also compensate disability of ADL!

## Slide 16: Terapia robótica: Miembros superiores
dedos
6+1 DoF
Lateralidad
Grados de libertad
Articulaciones Individuales
Miembro parético o no afecto de forma individual
Ambos brazos al mismo tiempo
Aumento de los grados de libertad
Una sola articulación
Combinación de articulaciones
codo
2 DoF
bilateral
unilateral

## Slide 17: Terapia Robótica: Miembros inferiores
Entrenamiento de la marcha
Ortesis activas
Sistema de soporte de peso
Exoesqueleto combinado con cinta de marcha
Apoyo en la posición y movimiento de las articulaciones de la pierna
Compensación de la debilidad y deformidades.
Cinta de marcha
plataformas
suelo
Sistema de soporte de peso
Sistema de efector final
El sistema de soporte de peso sigue al paciente
Permite una marcha natural pero requiere más actividad muscular
Notes: Diaz et al. 2011:
Treadmill gait trainers:
Developed to automate and improve partial body-weight support treadmill training so that the therapist’s labor is reduced. System is a combination of an exoskeleton and a treadmill.
Foot-plate-based gait trainers:
Feet of patients are placed on separate foot plates which are controlled by the robot to simulate different gait patterns.
Overground trainers:
Robots servo-follow the patients walking path overground. Patients have to move under their own control because there is no predetermined movement pattern.
Stationary gait trainers:
These devices train mainly leg strength and endurance as well as joint mobility and movement coordination.
Ankle and Knee Rehabilitation Systems
These systems try to restore ankle and knee motions. Stationary systems train patients without them having to walk. Active foot orthoses on the other hand are exoskeletons worn while walking overground or on treadmills. They control position and motion of the ankle, compensate for weakness or correct deformities to promote appropriate gait dynamics.

## Slide 18: Terapia robótica: Estrategias de control
  Control cooperativo con el paciente
  Movimientos guiados
  Apoyo parcial para iniciar y realizar el movimiento
  Simulación háptica para un entorno interactivo
  Espacio libre
  Interacción insignificante con el robot
  Guía total
  El movimiento predefinido lo realiza el robot
  No requiere de actividad muscular
Qué es un dispositivo háptico | 3D Systems
Notes: Physiotherapy/Movement therapy is based on extensive physical contact – interactions between robot and patient need to be controlled (safe, stable, gentle).
-Open-loop position control mode: Exact execution of predefined reference trajectories. Useful for severely affected patients which have troubles performing movements on their own. A down side is that muscle movements are only generated in a passive way  reduced active participation and training
-Closed-loop “assist-as-needed” control mode: Patient receives as much support or guidance as needed to complete a movement. This way patients are challenged as much as possible
-Force-fields: Introduces defined forces which can interfere with or assist a movement  possibility to create movement variability which is part of physiological movements
Loureiro et al. 2011:
Way rehabilitation robots should work:
Mimik human therapist behaviour. Be compliant when assisting movements, provide full support within the patient’s passive range of motion and nourish the patient’s confidence and motivation levels through goal-oriented informative biofeedback.
Passive systems often consist of mechanical linkages that move without much resistance when pushed or pulled.
Active systems are operated using traditional position control, moving a patients arm from point A to B using a certain velocity profile.
Interactive systems are often backdriveable and posses low, intrinsic, end point impedance.
Book: Introduction to Neural Engineering for Motor Rehabilitation
Challenge-based control:
Force-fields: Interfering or assisting forces. Provides movement variability.
Passive control:
Limb is constraint to a determined range of motion but else freely moveable.
For lightly affected patients in combination with gravity reduction.
Active control:
Robot moves patients limbs through a predefined path.
For severely affected patients that can’t move on their own. Reduced patient activity can limit learning.
Patient-cooperative control:
Provides assistance when performing a movement.
Provides challenges such as resistance and constraints on the unaffected limb.
Haptic simulation provides interactive environment
Path Control
•Path is like a virtual rail
•Patient controls timing of movement
•Robot applies assistive and corrective torques

## Slide 19: Terapia robótica: Ventajas
Terapia asistida por robot | Terapia convencional
Apoyo terapeuta | Limitado a la mano de obra
Alta fiabilidad | Menor repetición del movimiento
Altas cantidades de repeticiones / intensidad | Número limitado de repeticiones
Asistencia ajustable individualmente | Dificultades con pacientes gravemente afectados
Notes: Therapy duration, frequency
Therapy duration and frequency is often not adhering to proposed amounts from scientific knowledge but limited by the availability of therapists and staff. Robot-assisted therapy can improve that by freeing therapists from physically exhausting, manual work of guiding patients movements (conventional gait therapy often requires more than 3 therapists) so that therapists can focus on patients and therapy
Reliability and repetitions
Another limitation is the amount of repetitions that can be given by a therapist and the reliability of these repetitions. Robot-assisted therapy has the potential for giving more standardized therapy through precisely controllable, secure movements with increased number of repetitions and higher intensity.
Pros of robot-assisted therapy
-Ability to provide new objective and detailed assessment methods (kinematics and kinetics)
-Means of giving new interventions
  -Robots also have the potential to intelligently assist in accomplishing a much broader range of activities of daily living than is currently possible, including walking and manipulation tasks, improving independence and quality of life for many individuals with a severe disability.
Robotics in neurorehabilitation, Loris Pignolo, Eng 2009.
Evidence in rehabilitation points towards intensive and prolonged training. The problem with conventional therapy is that each therapist can only treat a single subject at a time which involves strenuous manual work. To improve the therapy robotic devices have been developed which can take over the manual labor of moving the patient. Over the last years these robotic therapeutic devices have become very elaborate adding a great amount of possibilities for improved therapy.
Robots also allow reliable quantitative measures of various physical properties over a wide range of variation (10, 11), with levels of speed, accuracy, power and endurance over time that are unachievable by humans. Reliability in the execution of repetitive tasks is high. What robots lack is the flexibility and adaptation, code-independent communication, high-level information processing, and detection of and responsiveness to weak and otherwise undetected significant sensory inputs which come with a human therapist.
Slides from Robert Riener:
Conventional Therapy
-Limited by availability of therapists.
-Poor reliability of repetitive tasks
-Limited number of repetitions.
-Impairment severity can prevent practicing
-Assessments can be subjective
-Poor motivation of patients.
-Unclear feedback regarding process
Robot-assisted Therapy
-Supports therapist -Frees from tedious, manual work
-Highly standardized therapy (precise, secure)
-High amounts of repetitions and intensity
-Intelligent assistance supporting as much as needed
-Objective assessments, measurement of undetectable quantities
-Highly motivated patients
-Detailed and timed sensory feedback
-New interventions (e.g. force field training)

## Slide 20: Terapia robótica: Ventajas II
Terapia asistida por robot | Terapia convencional
Valoraciones cuantificables y objetivas | Valoraciones imprecisas/subjetivas
Alta motivación para algunos | Motivación dependiente de la relación con el terapeuta
Feedback detallado | Feedback subjetivo
Nuevas intervenciones | 

## Slide 21: Terapia robótica: Limitaciones
Terapia asistida por robot | Terapia convencional
Coste (corto plazo) | Menor coste (corto plazo)
Precisa mayor espacio | Menores requerimientos de espacio
Riesgo de obsolescencia | «No riesgo de obsolescencia»
Sistemas específicos para miembros individuales | Tratamiento de cualquier parte del cuerpo
Carece de ciertos grados de flexibilidad y feedback | Grado alto de feedback y flexibilidad
Comunicación limitada | Comunicación dependiente del terapeuta
$
XL
Notes: Pros
Machine: Accurate assessment of physical measures within wide range of variability
Detection of physical measures undetectable to humans (e.g. electromagnetic waves)
Speed, accuracy, power
Memory storage
Endurance with accuracy over repetitive tasks
Reliability
Possible use in dangerous environments
Human: High-level cognitive processing and flexibility
More degrees of freedom
Accuracy in the execution of complex sensory motor tasks
Communication irrespective of coded language
Insight
Cons
Machine: No cognitive abilities or flexibility
Limited man/machine communication
Inability to respond to unpredicted events
Limited identification of salient features and recognition
Limited degrees of freedom
Human: Poorly reliable in repetitive monotonous tasks over prolonged periods of time
Limited speed and accuracy at high speeds
Variable performance depending on condition, motivation, attention, physiological and/or psychological factors/contingencies
Errors unavoidable
Limited detection of physical quantities
Inaccurate memory storage/retrieval
Slide from Roger Gassert
-Less costly (short-term)
-Not much space needed
-No risk of obsolenscence
-Therapist can treat most body parts
-High degree of feedback or flexibility through therapist
-Costly (short-term)
-Space consuming
-Risk of obsolenscence
-Limited to portions of affected limb
-Lacks degree of feedback/adjustment, flexibility and degree of freedoms
-Limited communication between robot and patient

## Slide 22: Nexo con los principios neurales y de aprendizaje
Nivel de dificultad óptimo
Repeticiones
Más repeticiones
Administración automática
Asistencia
Tiempo de práctica
Incremento de los tiempos de práctca
Menor necesidad de supervisión
Alta motivación
Dificultad adjustable individualmente
Añadir resistencia
Reducir soporte / asistencia
Notes:   Is able to deliver high amounts of repetitions in a single therapy session
  Is not affected by fatigue and can provide long duration
  Can provide variable practice schedules at arbitrary frequencies
  Can measure patient effort and challenge them accordingly
  Can be applied to train partial movements or specific limb segments (different devices)
  Is able to provide specific and functional training in combination with virtual reality
  Can have a high degree of variability and be adjusted to the individual patient
  Is highly motivating in combination with VR and exciting serious games
  Can provide instructions visually or auditory at specific times
  Can deliver haptic feedback through resistance or as sound or written text. Can be combined with FES to provide afferent feedback.
  Is able to guide severly affeted patients or assist mildly affected patients
Robert Riener – Lecture 8
• Support therapists against physical load
• More intensive training for patients (longer, more often, faster)
• New kind of motions and new kind of force support
• Highly repetitive, measureable, comparable, quantitative assessment
• Increased motivation applying audio-visual displays and games scenarios

## Slide 23: Nexo con los principios neurales y de aprendizaje
Feedback
Simplificar la práctica
Bilateral/unilateral
Movimientos parciales
Reducir los grados de libertad
Segmentación
Chart: 
| 1st Qtr | 2nd Qtr | 3rd Qtr | 4th Qtr
Sales | 4.2 | 2.8 | 2.3 | 2.1
Motivación
Incrementar motivación
Asistencia en función del éxito
Distintas formas de feedback
Feedback inherente y aumentado háptico
Asistencia según se requiera

## Slide 24: Sistemas no motorizados
2

## Slide 25: Sistemas sin motores
Los sistemas sin motores se desarrollaron a través de ideas de mejora de la terapia robótica
  Reducir la complejidad del Sistema y su coste.
  Mejorar la seguridad para los pacientes
  Mejorar el Entrenamiento de movimientos funcionales aplicados a actividades de la vida diaria.
Concepto:
motores
Sistema sin motores
-
=
Robot terapeútico
Notes: Neurorehabilitation Technology
Beginning in the late 1980s, engineering and rehabilitation research groups identified the potential to develop new technologies for upper extremity rehabilitation in neurologic disorders. A key realization was that rehabilitation technology had not yet taken full advantage of computers and robotic technology. Existing therapeutic equipment allowed people with arm weakness to practice arm movement, but it did so with limited flexibility, feedback, and engagement. For example, devices such as overhead slings, mobile arm supports, or simply a towel on a tabletop provided assistance in moving the arm against gravity, and devices such as elastic bands and hand exercise bicycles provided resistance for specific arm movements. Yet they had limited adjustability in the pattern of assistance, they could apply relative to that which was possible with a robotic device. Further, upper-extremity rehabilitation technology that was routinely used in clinics lacked sensors, with the notable exception of dynamometers. Adding sensors and then connecting the sensors to a computer would allow measurement and recording of arm movement ability, providing feedback to both the patient and therapist about progress. Further, once the sensed information was in the computer, then it could be used to control computer games, which allowed for the possibility of improving patient engagement in the exercises performed with the device.
Out of this rationale came several new robotic devices, including the MIT-Manus [ 1 ] , the MIME [ 2 ] , the ARM-Guide [ 3 ] , and the BiManuTrac [ 4 ] . Each device took the approach of assisting patients in making movements with the arm or forearm as they played simple computer games. Twenty years later, hundreds of patients have been involved in randomized controlled trials with these earlier devices, and two of these original devices are commercially available (MITManus and BiManuTrac 9 ] ). The studies indicate that people with an acute or chronic stroke can recover additional movement ability if they exercise for tens of hours with these devices; the transfer to functional movement is typically small [ 5– 7 ] . Exercise with a robotic device has also been found to be as effective or, in some cases, more effective than a matched amount of exercise performed with a therapist [ 2, 8, , or a matched amount of exercise performed with another rehabilitation technology, such as electromyogram triggered functional electrical stimulation [ 10 ] or sensor-based approaches to range of motion exercise [ 11 ]. Given these limitations in outcomes, developers of next generation technology for upper extremity therapy asked the question “How can we improve upon these initial robotic designs?” Many possible pathways have emerged, but three stood out to my group in the early 2000s. First, robotic devices were at the high end of complexity in the spectrum of therapeutic technology. While these devices were powerful tools for studying rehabilitation therapy, it was unclear whether their therapeutic benefit justified their cost. What had been demonstrated was the importance of repetitive practice of movement attempts, with or without robotic guidance present [ 12 ] . Further, installing motors on an orthosis or manipulandum (making the device robotic) increased cost and complexity and decreased safety. Therefore, we asked whether it would be possible to gain the benefi ts of robotic assistance without the robot. The second new pathway emerged out of the observation that initial robotic therapy devices did a relatively poor job of training functional movements. Functional movements are characterized by three features. First, they are oriented at achieving activities of daily living: prevailing robot therapies focused on simple range of motion and tracking games rather than simulating activities of daily living. Second, they often involve the use of many or all joints of the arm simultaneously; existing robots typically offered one or two degrees of freedom, with the exception of the MIME device, but this device relied on an industrial robot that did not match the workspace of the human arm. Third, functional movements typically require coordination of the hand with the arm to achieve a meaningful goal; existing robots typically worked on the arm or forearm in
isolation. At the same time, the importance of functional training was also being promoted by the broader fi eld of rehabilitation science. This position was infl uenced by both occupational therapy models in which functional practice is noted to hold greater meaning for a patient and by motor learning models in which transfer of learning is noted to be limited, and therefore, functional transfer would theoretically be maximized if patients spent therapy time practicing the activities they actually needed to relearn to do.
Whether assistance to movements is even necessary, as motor gains evidently depend largely on the efforts made by the participant. Robot-assisted movement
training for the stroke-impaired arm: Does it matter what the robot does?” [ 69 ] compared robotically assisted reaching with unassisted reaching in chronic stroke subjects. The two groups showed similar improvements, suggesting that the crucial factor in motor rehabilitation is not the assistance provided by a robot, but rather
the participant’s own voluntary efforts to move.
One kind of machines is driven by the force of the person using it, e.g., strengthening apparatus. These are considered as passive devices. Other systems include electric drives or other actuators, e.g., pneumatic devices, and can apply supporting, assisting, or resistance forces. Such actuated devices are referred to as active systems.
Rudhe et al. 2012
These non-robotic, gravity support systems are based on an ergonomic arm exoskeleton with integrated springs. Such devices cradle the entire arm, from shoulder to the hand, and counterbalance the weight of the patients’ arm. They enhance any residual function and neuromuscular control and assist active movement across a large 3-D workspace providing an augmented feedback [16]. As there are no actuators implemented in these devices, all movements are generated by the users themselves. The passive orthoses and robotic devices are equipped with sensors responsible for the assessment of their multiple degrees of freedom as well as to display the movement of different joints. Therefore, enormous amounts of data are collected during training that could be used not only to monitor the training session (intensity, duration, frequency etc.) but also to follow changes in the functional impairment. Recently studies have started to focus on the effectiveness of training with a gravity compensation device in different patient groups [16-18].
However, psychometric properties (reliability and validation) that account for clinical and patient-relevant aspects (such as the influence of the positioning of the
patient) have not been sufficiently addressed.
Spring-based orthoses, such as T-WREX and ArmeoSpring, are based on the rationale that functionally oriented activities, physical assistance in the form of gravity balance, and computer gaming and feedback will best promote movement recovery of the arm that is severely to moderately impaired after stroke. the patients recovered signifi cantly more arm movement ability than a control group that practiced tabletop exercises, a form of exercise which had diminished functional relevance, less-sophisticated mechanical assistance, and no gaming or objective feedback aspects. Further, the patients signifi cantly preferred exercising with T-WREX and could perform the exercises with only brief interaction with a supervising therapist. These results indicated that the starting rationale had at least some
validity. In addition, T-WREX was simpler, less expensive, and safer than a robotic device because it did not require actuators.

## Slide 26: Sistemas sin motores: Elementos
Soporte de peso
Mecanismo de equilibrio estático usando cables, muelles o alambres
Sensores
Medición de parámetros físicos: posición, fuerza, orientación y torsión
Interfaz paciente
Se une al paciente y transmite las fuerzas desde el sistemas: p.e cuffs
Interfaz usuario
Permite al usuario ajustar los parámetros
Interfaz paciente
Interfaz de usuario
Soporte de peso
sensores
Notes: In this exoskeleton device, springs support the human arm against gravity. The mechanical design allows the therapist to adjust the spring length and to select the proper amount of support. Sensors measure the position and orientation of the human arm, which is transmitted to the graphical display where the patient can see his own movement on the computer screen.
Arm support training – facilitates activation of agonists, possibly reduces abnormal coupling
Weight supported / passive orthoses / overhead sling suspension system
Generally composed of links and springs, static balancing mechanism using counter weights or springs or a combination of both.

## Slide 27: Sistemas sin motores: Miembros superiores / inferiores
Miembros superiores
Miembros inferiores
Sistemas de soporte de peso
Soporte de codo, dedos o muñeca
Soporte de peso estático
Soporte de la cadera, rodilla o tobillo
Notes: In therapeutic situations, therapists often apply full or partial support to a paretic limb or, in some instances to the trunk, to help reduce the effect of gravity on the patient’s motion. This is extremely difficult to do during a dynamic activity like walking, where the weight of the leg may create problems for the patient whose muscles are weak or lacks normal neuromuscular control due to a neurological insult.

## Slide 28: No motores vs. Sistemas robóticos
Sistemas sin motores
Dispositivos robóticos
  Guía del movimiento para una trayectoria óptima
  Apoyo del movimiento total, incluso para gravemente efactados
  Resistencia ajustable
  Caro y pesado
  Más complejo de usar
  Mayores precauciones de seguridad
  Coste significativamente menor
  Menor peso
  Más fácil de usar e intrísecamente más seguro
  Algunos no precisan fuente de alimentación
  Ninguna otra ayuda más que el soporte de la gravedad
  Sin correcciones del movimiento
  Resistencia limitada
Notes: Neurorehabilitation Technology
This training seems suitable for patients who can actively move the arm but suffer from reduced workspace and poor motor control.
Compared to motorized robots, this approach has the great advantage of significantly lower costs and weight. Moreover, the device is easier to use and intrinsically safe. The disadvantage is that it is not possible to support the patient other than against gravity, so, for instance, the device cannot support the patient in directed reaching movements, nor can it challenge the patient by resisting movement. Some devices overcome this by adding brakes to the robot that dissipate energy and challenge the patient’s movements. Current evidence suggests that nonmotorized devices might be very well suited for the training of mildly impaired stroke patients who do not need as much support as heavily impaired subjects.
- No external/internal power source needed
- No active feedback or movement correction/guidance
- Allows patients to move under their own control
- Preferable for patients that can move their limbs with little or no help
- No need for actuators
- Reduced system complexity and costs and increased patient's safety and acceptance level
Used to reduce or eliminate the effects of gravity and thereby allowing the user to effectively use his weak muscles for performing functional tasks like eating, drinking, or grooming. These devices may also help the patient retain or reestablish important proprioceptive information about the achievable workspace that the impaired limb should be able to reach as recovery progresses. Since the purely passive devices are relatively simple in their construction, they are affordable also for the patients themselves and are easy to use. The main disadvantage of these simple passive devices, which are mainly based on springs or counterweights, is that they basically provide a constant amount of weight reduction regardless of the position of the extremity. Even in positions of the arm, where less or no support is necessary, the patient is supported. Additionally, the desired movement trajectory cannot be predefined, and therefore the user may train a wrong, unphysiological
movement pattern. In the worst case, the patient cannot complete a desired movement at all. To overcome this limitation, passive devices are often used during occupational therapy sessions under supervision of a therapist, who actively supports the movements to ensure that a physiological movement trajectory is achieved.
However, they are often modified in the development process with more active characteristics. Still, the main characteristic that identifies a non-actuated or passive device is the lack of the ability to perform movement; they may be an option for continuation of the rehabilitation process, rather than for training of people with significant movement disorders at an early stage of rehabilitation.

## Slide 29: Sistemas sin motores: Ventajas
Sistemas sin motores | Terapia convencional
Apoyo terapeuta | Limitado a la mano de obra
Alto numero de repeticiones / intensidad | Número de repeticiones limitado
Asistencia en contra de gravedad | Asistencia del terapeuta de la gravedad
Valoraciones cuantificables y objetivas | Valoraciones imprecisas y subjetivas
Alta motivación para algunos | Motivación dependiente de la relación con el terapeuta
Feedback detallado y ajustable | Feedback subjetivo

## Slide 30: Sistemas sin motores: Limitaciones
Sistemas sin motores | Terapia convencional
Mayor espacio | Requerimientos de espacio menores
Riesgo de obsolescencia | No riesgo de obsolescencia
Sistemas específicos para miembros individuales | Tratamiento de cualquier parte del cuerpo
Menor flexibilidad y algunos tipos de feedback | Mayor grado de feedback y flexibilidad
Comunicación limitada | Interacción social
XL

## Slide 31: Estimulación eléctrica funcional (FES)
3

## Slide 32: Estimulación eléctrica funcional
Origen en la electroterapia
Originalmente se utilizó en neuroprótesis para sustituir la función afectada
Útil si los musculos y nervios están intactos
Estimulación eléctrica que proporciona contracciones musculares coordinadas y generan movimientos funcionales para estar de pie, caminar, agarrar, etc. (FES).
Dietz et al. 2012, Neurorehabilitation Technology
Concepto:
Patrón de electricidad
Estimulación eléctrica funcional
+
=
músculo
Notes: FES involves applying an electrical current, with electrodes on or close to the innervating nerve fibres. This generates an action potential which in turn produces a muscle contraction that can be modified by changing stimulus parameters laying the bases to restore functional movement. 2,4,7 An electrical field produced by the stimulating electrode depolarizes the cell membranes of neurons. The nerve is stimulated as it has a lower firing threshold than muscle. When depolarization reaches threshold, an action potential is produced by the influx of sodium from extracellular to intracellular space. The action potential travels distally to the neuromuscular junction and causes contraction of muscle fibres. The large motor units (type II) are activated first as they fire at a lower threshold. These are the motor units used for speed, power and tend to fatigue more quickly.
Neurorehabilitation Technology (Chapter 7)
Functional electrical stimulation was originally developed for the application as neuroprostheses to substitute impaired function. Over the years application changed to help retraining voluntary motor functions. There has been a change in thinking away from staying life-long dependent on FES towards shorter therapeutic usage termed functional electrical therapy which aims to improve voluntary function.
Functional electrical stimulation can be applied as long as there are intact muscles and nerves innervating them as well as joints and soft tissue supporting the muscle joint structures.
Simple joint movements elicited by electric stimulation is called neuromuscular electrical stimulation (NMES). A pattern of NMES that tries to create a coordinated body or limb movement compared to a muscle movement is called FES.
Electrical stimulation changes the potential across a nerve cell membrane and thus can elicit an action potential (induction of electrical charge in the immediate vicinity of the outer membrane of the cell).
Functional Electrical Stimulation (FES) has been used as a treatment modality for gait and chronic stroke since the 1960’s.1,2 Lieberson was one of the first to investigate the use of FES for foot drop.
Alon et al. 2013
The ability of FES to excite directly peripheral sensory and motor nerves is the principal physiological event leading to bidirectional propagation of action potentials. The excitation of sensory nerves results in the perception of tingling. The excitation of motor nerves leads to muscle contraction. The direct excitatory responses expand into numerous indirect responses affecting the peripheral neuromuscular, vascular, and articular (joint) systems while concurrently affecting the central nervous system (CNS).
Using surface electrodes, sensory nerve fibers are typically excited first. As the amount of the pulse’s electric charge increases (increase in stimulation intensity), more sensory fibers are depolarized, and the perception of tingling increase. When the pulse charge is sufficient, motor nerve fibers are also excited, and the muscle fibers innervated by the excited nerve fibers (motor units) contract [26]. Thus the perception of tingling and the muscle contraction are indirect responses to the excitation of the sensory and motor nerves respectively. As the intensity of stimulation (pulse charge) continues to increase, more nerve fibers are excited; the perception of tingling increases further and muscle contraction grows stronger, leading to joint motion. Thus the higher the intensity, the less comfortable is the perception of stimulation [31]. It is critical to recognize that the correlation between stimulation intensity and force of muscle contraction among patients is poor: some patients require low intensity to elicit very strong contraction, while others require high stimulus intensity that only elicits very weak contraction. Accordingly, the clinician must focus on the ability to achieve the desired contraction (and comfort perception) and not on the stimulator visual display of milliamps (or dial). From an electrophysiological perspective, the objective is to induce sufficient muscle contraction required to perform the task while keeping the sensory perception at a tolerable level.

## Slide 33: FES: Elementos
Estimulador
Determina la fuerza de estimulación (corriente o voltaje) frecuencia y longitud de la onda.
Electrodos
Aplicación del voltaje a la piel
Fuente de alimentación
Proporciona electricidad para dar la estimulación
Fuente de energía
estimulador
electrodos
Notes: Stimulators
These control the current or voltage 10
- With voltage regulated stimulators the amount of delivered current is dependent on electrode interface impedance 10
With surface electrodes, as the electrodes dry or lose contact with skin, the impedance increases and the current flow decreases thereby10 reducing the risk of burns6,10
- Due to the electrode-skin interface and variable impedance, the motor response is less consistent10
- Used with surface or transcutaneous electrodes6
- Current is better regulated and not affected by impedance with current regulated stimulators10
- Used with implanted electrodes6,10
- More consistent motor response10
Biomaterials
natural or synthetic material that is suitable for introduction into living tissue (medical device)
Proximity of electrode and nerve reduces the intensity of stimulation required for axonal excitation
Electrode advantages
Reduction of hazardous electrochemical processes and power consumption of the stimulator system
Minimal mechanical distortion of the electrodes during movement,reducing the chances for lead failure
The electrical characteristics are not affected by changes in muscle length during movement
Selective stimulation of fascicles within the nerve is possible,by multiple-contact electrodes and by manipulating the stimulation pulse parameters
Recording of nerve electrical activity can be achieved with the same electrodes
Electrode disadvantages
Nerves can be damaged by the implanted electrode
Implantation requires delicate surgical procedure, depending on the accessibility of the nerves
Reverse order of recruitment of motor units during electrical stimulation leading to fast-fatigue production
Selective stimulation requires careful testing after implantation given the variability in fascicular architecture of each peripheral nerve
Alon et al. 2013
the most advanced FES are wearable systems that incorporate the latest in bio-compatible materials interfacing with the body, micro-electronic infra-structure, small and fast recharging batteries, and software-driven selection of parameters as well as functional and task-specific training programs. Few FES systems also incorporate “intelligent” software that monitors patient performance and automatically adjusts the stimulation as the task or functional activity changes, or automatically adjust to account for changes in terrain while walking [60,61].
Bio-compatible materials refer mostly to the electrodes, and the material used to secure them to the body. The typical self-adhesive electrodes may soon be replaced with water-soaked, highly absorbent fabric to further minimize skin irritation and improve the comfort of stimulation. The wearable system’s material should also be easy to clean to minimize bacterial and other contamination. This is particularly important for patients who depend on the FES for several hours every day. Wireless FES means that the typical lead wires have been eliminated- a major practical and cosmetic improvement. Wireless may also mean that communication between the stimulator, the sensors that control the stimulation, and the programming of the stimulator to set the individual patient’s treatment and functional activities are all done wirelessly. Wireless communication makes the patients’ evaluation and training considerably faster, saving the clinicians’ precious time. It likewise dramatically improves the ease of at-home use for the patient. “Intelligent software” could have diverse meanings, and the astute clinician should learn the specific meaning from the product’s manufacturer.
Hamid et al. 2008
Both nerves and muscle fibres respond to electric current. However, for practical purposes FES is used to directly stimulate nerve fibres only, as a much lower amount of current is required to generate an action potential in a nerve than the one required for muscular depolarisation.
The main component of a FES system is the microprocessor-based electronic stimulator which determines when and how the stimulation is provided, with channels for delivery of individual pulses through a set of electrodes connected to the neuromuscular system. The microprocessor contains programs for sitting, standing, walking, hand grasp etc. It serves to generate a train of impulses that grossly imitate the neural triggers that would have normally passed through the spinal cord to the appropriate peripheral nerves below spinal cord lesion for these different programs. These stimuli thus trigger action potentials in the peripheral nerves which inturn activate muscle contractions in the associated muscles fibres [72]. The pulse amplitude (magnitude of current), duration, frequency, waveform (a display of a signal on an oscilloscope that shows the magnitude of current or voltage with respect to time) and duty cycle (the total time to complete one on/off cycle) regulate the stimulation parameters. The numbers of channels, which can range from one to several, govern the sophistication required for complex outputs like FES assisted standing.
The programmable microprocessor activates the various channels sequentially or in unison to synchronize the complex output of the stimulator. Electrodes provide the interface between the electrical stimulator and the nervous system. Various types of electrodes have been developed and are available ranging from non-invasive surface electrodes to invasive implantable ones. Implantable electrodes provide more specific and selective stimulation to the desired muscle group than the surface electrodes. The feedback control of the FES system can be either open-looped or closed-looped. Open-looped control is used for simple tasks such as for muscle strengthening alone, and requires a constant electrical output from the stimulator. In a closed-looped system, the parameters for electrical stimulation are constantly modified by a computer via feedback information on muscle force and joint position thus stimulating various muscle groups simultaneously leading to a combination of muscular contraction needed for a complex sophisticated functional activity such as walking [34]. Paraplegic patients using FES for ambulation still require the use of walker or other orthotic devices for stabilising the ankle, knees and hips.
Most FES systems are basically quite similar in design and purpose, but the electrical stimulation may be delivered either by surface (transcutaneous), percutaneous or implanted leads and electrodes. The main components of FES systems (Figure 1) include a portable power source (rechargeable battery), command microprocessor/control unit, stimulator, lead wires, electrodes and sensors.18 Surface FES systems have electrodes that are placed on the skin over the desired nerves or their motor points and these are connected by lead wires to the stimulator, which is carried by the user. Surface FES systems can be safely used by clinicians and are relatively inexpensive, but accurate placement of the electrodes may be difficult and time consuming. It may not be possible to generate isolated contractions of specific muscles and deep muscles may not be activated at all. Additionally, surface stimulation may be painful and the systems visible appearance may be cosmetically unacceptable. Although surface FES system's are adequate for therapeutic or short-term use, implantable systems seem more desirable for long-term use.
Intramuscular electrodes with percutaneous leads have mainly been used during the development of implantable FES systems. To date, they are not part of any FES systems approved for clinical use, but they are undergoing clinical trials for shorter-term muscle conditioning paradigms, such as for relief of pain in shoulder subluxation. They may be inserted through the skin with a large gauge hypodermic needle and placed at the motor point of the desired muscle. When the needle is withdrawn, the electrode remains with the lead wire exiting through the skin and connecting with an external stimulator. In general, percutaneous lead wires appear safe, but with prolonged use, utmost caution is necessary to prevent infection and granuloma formation.19
Implanted FES systems are ideal for long-term use. Here, the electrodes, lead wires and stimulator are implanted, but the control unit and the rechargeable battery power source are external. The stimulator receives commands and power through a radiofrequency telemetry link (antenna) from the control unit and batteries respectively, but these are usually externally placed. Unfortunately, the power demands of multichannel FES systems are too great to permit the use of implantable batteries using current technology. Voluntary activation of the system is achieved via external transducers or switches connected to the control unit. The implanted electrodes are surgically placed adjacent to a nerve (epineural), around a nerve via helix or a cuff, or at the motor point on the muscle surface (epimysial) or within the muscle itself (intramuscular). Nerve-based electrodes provide good muscle specificity and allow stimulation of specific muscles and excellent recruitment with relatively low electrical currents. Care must be taken during the surgical procedure and during long-term stimulation at relatively high frequencies to avoid damage to the nerve. Fortunately, guidelines for safe stimulation have been developed and these electrodes have been used successfully in many applications, such as control of bladder, phrenic nerve for breathing, peripheral nerve stimulation for pain control, and cranial nerve stimulation for epilepsy suppression. Epimysial electrodes generate minimal damage and have proven to be durable for upper and lower limb applications,20, 21 but for activation of deep and very small muscles, intramuscular electrodes are preferable.
Normal motor activity depends not only on synchronized muscle contractions but also on a highly sophisticated sensory feedback processed through innumerable sensory end organs, sensory nerves, the spinal cord and the brain. Unfortunately, modern medical technology does not even come close to providing such sensory information, which is a major shortcoming of multichannel FES systems. Relatively primitive sensory feedback signals from the limbs can be obtained from externally placed goniometers and potentiometers placed at various joints. These can measure joint positions and motion, permitting the systems microprocessor to calculate the velocity and acceleration of movement and consequently adjust and control the stimulator.
The user and the control unit operate the FES system in an interactive fashion. The control unit, which is located external to the body in all currently used FES systems, contains the system's microprocessor (computer, intelligence) and usually the battery. It has three main functions:13 (a) supplies power from its batteries to the entire system; (b) extracts information from the user and the sensors; and (c) transforms the received information into commands that are transmitted by radiofrequency signals through an externally located transmitting coil to the implanted stimulator. The user is able to control the entire system by varieties of sources, such as a joystick or switches that may use breath force, myoelectric signals, and voice recognition or motion sensors. Depending on the feedback and automatic control provided by the system, the control can be classified either as open loop or closed loop. In an open loop control, preprogrammed patterns of electrical stimulation are individually created for a specific function without automatic correction for changes in muscle force or joint motion. In a closed loop control, the control unit receives information on muscle force and joint motion from the sensors and automatically modifies the electrical stimulation.23
Several criteria for effective application of FES have been identified as follows:13 (a) the strength of the FES-induced muscle contraction must be forceful, controllable and repeatable; (b) the electrical stimulus must not be painful; (c) the LMN must be intact and the neural structures must not be damaged by the FES; and (d) the method of FES delivery must be acceptable to the user. These criteria must be considered when the various methods of applying electrical stimulation are selected for functional purposes.

## Slide 34: FES: Parámetros de estimulación
Frecuencia de pulso
  Contracciones suaves vs serie de espasmos.
  Una frecuencia más alta provoca contracciones más fuertes pero los músculos se cansan antes.
  Frecuencia ideal: 12-16 Hz (superior) and 18-25 Hz (inferior)
Pulso amplitud/duración
  Incrementar la amplitude del pulso o la duración incrementa la fuerza de contracción.
  Amplitudes demasiado altas provocan dolor nervioso.
  Duración 200-400 us
Notes: Set up and Parameters
In order to have a flow of current, 2 electrodes are required. The electrode arrangement can be monopolar or bipolar.6,10 Monopolar – the active electrode (tends to be a smaller electrode) is positioned by the peripheral nerve, the indifferent or return electrode is positioned over less excitable tissue (tendon or fascia).6,10 In a multichannel monopolar system, there is only one indifferent electrode and several active electrodes.10 Bipolar –the active electrode is also positioned by the nerve to be stimulated and the indifferent electrode is placed close to the active electrode. In a multichannel bipolar system, for each active there is an indifferent electrode. This may provide a more selective area of muscle activation.6,10
Provision of electrical stimulation is in a waveform of electrical current pulses. The strength of the muscle contraction is controlled by the pulse frequency, amplitude and duration of the current pulses.
Pulse frequency
- Need a high enough frequency, fusion frequency, to create a smooth contraction. Too low and you produce a series of twitches (at least 12-15 Hz to achieve fused muscle response. [6,10]).
- The higher the stimulus frequency, the stronger the contraction but the muscle also fatigues more quickly. [6,10]
- Optimal stimulation frequency: 12-16 Hz for upper extremity and 18-25 for lower extremity. [6]
Pulse amplitude and duration
- Increasing pulse amplitude or pulse duration activates a greater number of axons and motor units due to the larger electrical field produced by the larger charge.  increases the strength of contraction. [6,10]
- Amplitude beyond motor threshold also excites small diameter unmyelinated C fibers which elicit pain [10]
- Pulse duration of 200-400, 300 us appears to be more comfortable 10
Waveform
- Monophasic – repetitive unidirectional pulse, which is primarily cathodic or negative
phase
- Biphasic – repetitive pulse with a cathodic then anodic (positive) phase
- The first phase brings about the action potential
- The second phase balances out the charge to prevent tissue damage which is key when using implanted electrodes
Stimulation delivery
- Surface – electrodes are placed over nerves or motor points6,10
- Noninvasive, easily applied, somewhat inexpensive, easily used in clinic settings10
- Repeated consistently accurate electrode placement can be difficult6,10
- Can be painful with sensitive skin6,10
- Challenging to attain deep muscle activation or specific muscle contraction
- Aesthetics and management of a system with multiple components6,10
- Electrodes can shift or fall off while limb is moving6
- Percutaneous – use electrodes that are implanted into isolated muscles with hypodermic needle10
- Provide activation for deep muscle, repetitive accurate muscle contractions6,10
- Require lower stimulation currents6
- Less painful6,10
- Exit site of electrode lead must be kept clean6
- Risk of breakage or infection6
- Last for up to 3 months6
- Used for trial before implantable systems surgery6
- Implantable systems – electrodes and stimulator are implanted6,10
- An external control unit provides power and instruction through a radio-frequency telemetry link
- Electrodes can be implanted on or in the muscle, beside or around a nerve6,10
- Good for wide, thin or superficial muscle6
- Increased specificity of muscle stimulation6.10
- No surface wires, a small antenna is taped over the stimulator site10
- Risk of tissue growth affecting the nerve6
- Long term use10
Example of parameter settings.
Modulation: Pulse or burst
Amplitude: maximum tolerated
Pulse Duration: 100-300 us
Frequency: 20-100
Duty cycle: on:off 2:10 or 5:15
Number of contractions: 10-20 at maximum intensity, 15minutes session 2-3x day
Frequency : 3-7x week 11
Parameters for depolarisation of intact peripheral nerve fibres
Pulse width 0–500µs
Frequency 10-50Hz
Current 0-250mA
Parameters for activation of denervated skeletal muscles
Pulse width 10-300ms
Frequency 16-25Hz
Current +/- 250mA

## Slide 35: FES: Electrodes
Electrodos de superficie
Electrodos sub cutáneos
No invasivos
Necesita de un medio de conducción de la corriente (agua o gel)
pericutáneo
implantado
Insertado a través de la piel
temporal
Implantado debajo piel
permanente

## Slide 36: FES: Electrodos de superficie
Ventajas
Método no invasivo
Varios músculos pueden ser estimulados con un solo electrodo
Fácil de aplicar y barato
$
Desventajas
Pobre selectividad
No es posible estimular músculatura más profunda
Respuesta de estimulacion variable, necesitando tiempo para re posicionar los electrodos
Se requiere un mayor voltaje
Notes: FES systems used today stimulate the nerves or the points where the junction occurs between the nerve and the muscle. The main reason is the fact that direct muscle stimulation requires considerably more energy to generate contractions which complicates the whole system (safety concerns etc.).
The electrical charge can stimulate both motor and sensory nerves.
Typically, one “wave” of action potentials will propagate along the axon toward the muscle (orthodromic propagation), and concurrently, the other “wave” of action potentials will propagate toward the cell body in the central nervous system (antidromic propagation). The antidromic stimulus has been considered an irrelevant side effect of FES. However, in recent years, a hypothesis has been presented suggesting the potential role of the ant idromic stimulation in neurorehabilitation [ Rushton et al. 2003, Functional electrical stimulation and rehabilitation--an hypothesis ].
Two types of electrodes exist, surface or subcutaneous (percutaneous or implanted). Surface electrodes are placed on the skin surface above the nerve or muscle that needs to be “activated.” They are noninvasive, easy to apply, and generally inexpensive. Due to the electrode-skin contact impedance, skin and tissue impedance, and current dispersion during stimulation, much higher-intensity pulses are required to stimulate nerves compared to the subcutaneous electrodes. A major limitation of the transcutaneous electrical stimulation is that some nerves, for example those innervating the hip flexors, are too profound to be stimulated using surface electrodes. This limitation can be partly addressed by using arrays of electrodes which can use several electrical contacts to increase selectivity.
Subcutaneous electrodes can be divided into percutaneous and implanted electrodes. The percutaneous electrodes consist of thin wires inserted through the skin and into muscular tissue close to the targeted nerve. These electrodes remain in place for a short period of time and are only considered for short-term FES interventions. One of the drawbacks of using the percutaneous electrodes is they are prone to infection and special care has to be taken to prevent such events. The other class of subcutaneous electrodes is implanted electrodes. These are permanently implanted in the consumer’s body and remain in the body for the remainder of the consumer’s life. Compared to surface stimulation electrodes, implanted and percutaneous electrodes potentially have higher stimulation selectivity with much less electrical charge applied, both of which are desired characteristics of FES systems. To achieve higher selectivity while applying lower stimulation amplitudes, it is recommended that both cathode and anode are in the vicinity of the nerve that is stimulated. The drawbacks of the implanted electrodes are they require an invasive surgical procedure to install, and, as is the case with every surgical intervention, there exists a possibility of infection following implantation.
The implanted FES systems are primarily used as permanent neuroprostheses. On the other hand, the surface FES systems have been used equally well as neuroprostheses and platforms to deliver FET.
Surface: selbsthaftende Elektroden aus leitfähigem Gewebe und mit leitfähigem Polymer beschichtet + externer Stimulator
Electrode quality (surface ES - uniform conductivity, conformity to irregular body parts, durability, and hydration) is a pre-requisite determinant of successful stimulation.
Poor quality electrodes lead to uncomfortable, ineffective ES
Position and size of the surface electrode determine perceived comfort, as well as the specificity of the ES.
Muscles such as the upper limb supinator are difficult to stimulate with surface electrodes.
Lower limb: Implanted electrodes are generally inserted in to the epineruium of the peroneal nerve under general anaesthesia. The electrodes are either percutaneous (passed through the skin and connected to an external pulse generator) or fully implanted (controlled by radiofrequency waves).
Surface electrodes
Requires no anaesthesia and can fitted on an outpatient visit. The electrodes are placed over the nerve and are connected by leads to a stimulator unit and controlled by a foot switch. The disadvantage is that the electrodes need to be positioned by the patient.
Alon et al. 2013
To maintain good quality, surface electrodes should be replaced often, thus adding to the cost of FES utilization. All clinicians involved with FES must be aware that maintaining good quality electrodes is vital to assure successful outcomes.
Electrode quality (uniform conductivity, conformity to irregular body parts, durability, and hydration) is a pre-requisite determinant of successful stimulation. Poor electrode quality is the primary determinant of uncomfortable, ineffective stimulation, and in fact the most likely cause of skin irritation and even skin burn regardless of the FES system used (Taylor et al. (1999) Clinical audit of 5 years provision of the Odstock dropped foot stimulator).
The position and size of the surface electrodes contribute to the perceived comfort of stimulation. The size should not be too large or too small and the position must be correct to assure contraction only in the target muscle group.
Some muscles cannot be reached effectively with non-invasive FES

## Slide 37: FES: Electrodos subcutáneos
Ventajas | 
Pericutáneo | Implantado
Buena selectividad | 
Respuesta de percepción del estímulo constante | 
Menor voltaje requerido | 
Desventajas | 
Pericutáneo | Implantado
Cirugía invasiva | 
Seguridad (riesgo de infección, que partes del electrodo se dañen) | 
Notes: Percutaneous electrodes
Inserted through skin
For temporary placement
Implanted electrodes
Implanted permanently
FES systems used today stimulate the nerves or the points where the junction occurs between the nerve and the muscle. The main reason is the fact that direct muscle stimulation requires considerably more energy to generate contractions which complicates the whole system (safety concerns etc.).
The electrical charge can stimulate both motor and sensory nerves.
Typically, one “wave” of action potentials will propagate along the axon toward the muscle (orthodromic propagation), and concurrently, the other “wave” of action potentials will propagate toward the cell body in the central nervous system (antidromic propagation). The antidromic stimulus has been considered an irrelevant side effect of FES. However, in recent years, a hypothesis has been presented suggesting the potential role of the ant idromic stimulation in neurorehabilitation [ Rushton et al. 2003, Functional electrical stimulation and rehabilitation--an hypothesis ].
Two types of electrodes exist, surface or subcutaneous (percutaneous or implanted). Surface electrodes are placed on the skin surface above the nerve or muscle that needs to be “activated.” They are noninvasive, easy to apply, and generally inexpensive. Due to the electrode-skin contact impedance, skin and tissue impedance, and current dispersion during stimulation, much higher-intensity pulses are required to stimulate nerves compared to the subcutaneous electrodes. A major limitation of the transcutaneous electrical stimulation is that some nerves, for example those innervating the hip flexors, are too profound to be stimulated using surface electrodes. This limitation can be partly addressed by using arrays of electrodes which can use several electrical contacts to increase selectivity.
Subcutaneous electrodes can be divided into percutaneous and implanted electrodes. The percutaneous electrodes consist of thin wires inserted through the skin and into muscular tissue close to the targeted nerve. These electrodes remain in place for a short period of time and are only considered for short-term FES interventions. One of the drawbacks of using the percutaneous electrodes is they are prone to infection and special care has to be taken to prevent such events. The other class of subcutaneous electrodes is implanted electrodes. These are permanently implanted in the consumer’s body and remain in the body for the remainder of the consumer’s life. Compared to surface stimulation electrodes, implanted and percutaneous electrodes potentially have higher stimulation selectivity with much less electrical charge applied, both of which are desired characteristics of FES systems. To achieve higher selectivity while applying lower stimulation amplitudes, it is recommended that both cathode and anode are in the vicinity of the nerve that is stimulated. The drawbacks of the implanted electrodes are they require an invasive surgical procedure to install, and, as is the case with every surgical intervention, there exists a possibility of infection following implantation.
The implanted FES systems are primarily used as permanent neuroprostheses. On the other hand, the surface FES systems have been used equally well as neuroprostheses and platforms to deliver FET.
Percutaneous: Dünner Drahtwendel mit Widerhaken wird durch die Haut in den Muskel in die Nähe des motorischen Punktes eingeführt
Implanted: Epineutrale Plättchenelektroden, epineutrale Drahtschleifenelektroden, Manschettenelektroden um einen Nerv + implantierter Stimulator

## Slide 38: FES: Applicación
Neuroprótesis
Neuromodulación
Funciones perdidas (caminar, agarre) se recuperan a través de señales eléctricas que reemplazan los comnados motores o las señales aferentes
Open-loop
Closed-loop
Estímulo pre programado sin feedback sensitivo
El feedback sensitivo ajusta la intensidad del estímulo para controlar el movimiento
Nerve activity is altered through the delivery of electrical stimulation to normalize or modulate nerve function.
Notes: http://www.fescenterindia.com/how-can.html
a) Foot Drop (Neuroprosthetic)
b) Sit to stand training
c) Pre-gait training
d) Hemiplegic gait/ circumductory gait
e) Shoulder subluxation
f) Hand function such as grasp and release, drinking water etc.
g) Along with other treatment as along with treadmill training
h) strength training
During FET central nervous system essentially relearns how to control the impaired muscles and how to contract them in a temporarily appropriate manner to generate the desired body function.
Consumers who use FES on a regular basis experience significant carryover in function that persists even when the device is not in use – this effect has been termed “carryover effect”.
Peripheral mechanisms of FES can be:
Improved muscle function through muscle training (strengthening)
Voluntary function improvement through increased flexibility and range of motion
Reduction of spasticity which results in improved motor function
Why use FES?
For CNS activity dependent plasticity, the critical principles of motor learning are “close to normal movements, muscle activation during practice of movement, focused attention, repetition of desired movement, training specificity.”
Research has shown us that recovery is aided by motor experience. Repetition of movements has also been identified as a key in motor relearning.1,3,5,6,9 FES may facilitate motor recovery with muscle and joint afferent feedback with repetitive movement.10 Peripheral stimuli can influence reorganization in the brain.3,5 The afferent and efferent input from movement facilitated by FES can play an important role as a reminder on “how to perform movement properly.”1 Daly and Ruff8 support FES as fulfilling the motor learning principles for gait. FES can closely reproduce the motor components of gait (close-to-normal movement and repetition).
FES induces electrical impulses in the stimulated nerve that evokes action potentials to ‘replace’ the signal that would have come from the CNS.
Loss of joint range of motion (ROM) is a common impairment of the musculo-skeletal system consequent to immobilization. The restriction of normal range is typically brought about by shortening and adhesion formation in soft tissues surrounding the joint, and in the case of damage to the brain by uncontrolled activation of muscles. Maintaining or restoring ROM has been achieved with the use of FES [5,14,41-43,48] The mechanism is a simple biomechanical proposal. The electrically induced contraction force translates at the joint into torque (moment of force), and the joint moves, overcoming the opposite toque generated by the shortened soft, connective tissues.
Hemiplegic gait
gait in which the leg is stiff, without flexion at knee and ankle, and with each step is rotated away from the body, then towards it, forming a semicircle.
Synonym(s): circumduction gait, spastic gait
Nerve vs Muscle Stimulation
  Upper motor neuron lesion (spastic paraplegia) – Nerve Stimulation (the most common form of FES)
  Lower motor neuron lesions (denervated muscles) – Muscle Stimulation
Orthotic vs therapeutic usage
Surface vs implanted systems

## Slide 39: FES: Ventajas y limitaciones
Ventajas
Producción de «movimientos naturales»
Reemplaza el feedback dañado o perdido
Prevención de la atrofia muscular, incremento de la fuerza
Se puede utilizar en el hogar
Limitaciones
Fatiga muscular
Irritación de la piel
Tolerancia variable al estímulo / dolor
Dificultad en la colocación precisa de los electrodos
Notes: Functional Electrical Stimulation: Standing and Walking After Spinal Cord Injury
Advantages page 8.
Movements evoked by FES use the patient’s own muscles and metabolic energy.
Contraindications:
Poor skin condition
Poorly controlled epilepsy
A history of significant autonomic dysreflexia in incomplete spinal cord injury above T6
Pregnancy
Active medical implants such as cardiac pacemakers or other devices
Patients with a cancerous tumour in the area of the ES should be excluded as increased local blood flow may increase tumour growth
Patients with exposed orthopaedic metal work in the area of ES
Contraindications
- Pacemaker
- Peripheral vascular disease if possibility of causing thrombi to loosen
- Hypertension or hypotension can affect autonomic responses
- Areas of excessive adipose tissue increase impedance
- Neoplastic tissue
- Active infection
- Devitalized skin due to xray therapy
- Cognitive issues affecting ability to provide feedback
- Not over carotid sinus
- Not over thoracic region
- Not over phrenic nerve
- Not over trunk if pregnant 11
Several contraindications
Muscle fatigue – increases with increased frequency and intensity of stimulation4,7
 Pain4,6
 skin irritation4
 unrealistic expectations4
 multichannel surface systems can be cumbersome to apply and wear7,8
 accurate electrode placement6,7
Some of the difficulty with using FES for the hemiplegic shoulder are:
- Cutaneous pain receptors are stimulated which affects tolerance and compliance
- Difficult to activate deep muscles
- Difficult to control the level of contraction
- Accurate electrode placement and finding the stimulation parameters that are
tolerated and achieve the desired affect requires skill and experience6
Alon et al. 2013
It is not possible to move the shoulder and various other joints through its full range of motion. A main reason is that most FES systems only offer 2 channels thus enabling concurrent stimulation of only 2-3 muscles out of at least a dozen needed for full flexion or abduction [30]. Another reason is that some muscles are inaccessible due to being located very deep or covering by different muscles. .
Involuntary muscle activation because of spasticity and unstable joints as a result of damage to the brain further limit ROM of some body parts (shoulder, hip). Some muscles also require very strong contraction that most patients could not tolerate particularly if the electrodes are small relative to the size of the muscle mass. Collectively, the limited ROM FES can generate is closely associated with subject inability to tolerate the inevitable sensation that accompanies the contraction.
Whereas most patients can be conditioned to tolerate the stimulation, individual patients’ tolerances vary considerably, and all patients can only tolerate so much (Alon and Smith 2005).
Finally, FES appears minimally effective in generating movements along longitudinal axis such as pronation-supination of the forearm, external-internal rotation at the gleno-humeral joint and at the hip.
The safety of using FES is not known during pregnancy and thus should not be used, and FES is contra-indicated if the patient also has an implanted electronic device (non-invasive FES). FES should not be applied over irritated or open skin lesions as it is likely to increase irritation and further damage the lesion. In frequently, patients may become dizzy, have shortness of breath, or develop temporary headaches. Clinicians must be aware of these rare episodes and stop the stimulation if the patient reports any unwanted response.

## Slide 40: Tecnología de sensores
4

## Slide 41: Tecnología de sensores
Las condiciones demográficas plantean una serie de cuestiones básicas:
¿Cómo nos ocupamos del incremento de personas con condiciones médicas complejas?
¿Cómo Podemos mejorar la calidad de la atención en aquellas zonas con menor acceso?
¿Cómo incrementamos la independencia y participacion de personas con discapacidad?
“Un aparato que mide o detecta las condiciones del mundo ral, tales como el movimiento, el calor, la luz y las convierte en una representación analógica o digital.”
Free Online Encyclopedia
Concepto:
monitor
Tecnología de sensores
+
=
sensor

## Slide 42: Tecnología de sensores: Elementos
Hardware sensores y recolección de datos
Para recoger datos de movimiento y fisiológicos
Software de comunicación con hardware
Para retransmitir los datos a un centro remoto
Técnicas de análisis de datos
Para extraer la información clínicamente relevante de los datos fisiológicos y de movimiento.
Software de comunicación con hardware
Hardware sensores y recolección de datos
Técnicas de análisis de datos

## Slide 43: Tecnología de sensores: Factores habilitantes clave
Micro Fabricación
Miniaturización
Sistema en chip
Bajo coste
Tecnología móvil
Puerta de enlace
Localización
Computación
Tecnología comunicación
Baja energía
Estándares Wireless

## Slide 44: Tecnología de sensores: Campo de aplicación
Sensores fisiológicos y de movimiento
Sensores biomecánicos
Sensores de movimiento y fisiológicos
Aplicaciones diagnósticas
Aplicaciones monitorización
Tratamiento en curso
Notes: Patel S, park H, Bonato P, Chan L, Rodgers M (2012) A review of wearable sensors and systems with application in rehabilitation. Journal of NeuroEngineering and Rehabilitation, 9:21
Physiological monitoring could help in both diagnosis and ongoing treatment of a vast number of individulas with neurological, cardiovascular and pulmonary diseases such as seizures, hypertension, dysrthymias and asthma.
Home based motion sensing might assist in falls prevention and help maximize an individual’s independence and community participation. Remote monitoring systems have the potential to mitigate problematic patient access issues

## Slide 45: Tecnología de sensores en rehabilitación I
Salud y bienestar
Monitorización
Rehabilitación en el hogar
Monitorización de la actividad
Detección de caídas o problemas cardíacos
Ejercicio terapeútico
«Gerontología ambiental»
Combinación con realidad virtual

## Slide 46: Tecnología de sensores en rehabilitación II
Valoración de la eficacia del tratamiento
Detección temprana de alteraciones
Manejo de la enfermedad
Estado del paciente
Alcanzar una detección temprana de cambios en el estado del paciente que requieren de intervención clínica.
Ajustar las intervenciones de tratamiento en base a las necesidades del paciente.

## Slide 47: Tecnología de sensores: Ventajas y limitaciones
Ventajas
Asequible para la mayoria de los pacientes
Soluciona problemas de acceso a la rehabilitación (pacientes que viven lejos de las clínicas)
Incrementa la independencia y participacion del paciente
Limitaciones
Barreras técnicas como por ejemplo las limitaciones de las baterías de los sensores
Barreras culturales asociadas al uso de dispositivos medicos en el hogar.

## Slide 48: Realidad virtual
5

## Slide 49: Realidad Virtual
La idea de utilizer realidad virtual en rehabilitación surge en la mitad de la década de los 90
  La trayectoria definida en el entorno virtual debe ser realizada por el paciente (Holden et al. 1999)
  Incrementar la motivación y simplificar el feedback (feedback de ejecución)
“La realidad virtual se refiere al uso de estimulaciones interactivas creadas con un hardware y software de ordenador para presentar a los usuarios oportunidades de interaccionar con entornos que se vean y sientan similares a los que suceden en la vida diaria.”
Weiss et al. 2004
Concepto:
monitor
Realidad virtual
+
=
input/usuario o dispositivo seguimiento
Notes: Weiss PL, Rand D, Katz N, Kizony R (2004) Video capture virtual reality as a flexible and effective rehabilitation tool. J Neuroeng Rehabil 1 (1):12
Holden MK, Todorov E, Callahan J, Bizzi E (1999) Virtual environment training improves motor performance in two patients with stroke: case report. Neurology Report 23, 57-67
Virtual enviornment:
http://clipartist.net/svg/monitor-screen-may-2011/
Virtual reality device:
http://products.iisartonline.org/
Kiper lecture
Virtual Reality refers to a high-end user interface that involves real-time simulation and interactions through multiple sensory channels.
Why use VR: VR is able to immerse you in a computer-generated world of your own making: a room, a city, the interior of human body. With VR, you can explore any uncharted territory of the human imagination.
Image (immersion glove)
http://cb.nowan.net/blog/state-of-vr/state-of-vr-devices/#haptics

## Slide 50: Modelo de RV basado en la rehabilitación
El objetivo es ayudar al paciente a conseguir la participación en el mundo real, superando, adaptando o minimizando las barreras del entorno.
Transferencia de destrezas o tareas entrenadas del entorno virtual al mundo real.
Ejecución de la tarea en el entorno virtual
Mundo real
Fase de transferencia
«Espacio de interacción»
Ejecución en el mundo real
Actividad
Participación
Notes: The virtual reality experience is multidimensional and appears to be influenced by many parameters whose interactions remains to be clarified. A proposed model for virtual reality in rehabilitation is presented on this slide. This model was developed within the context of the International Classification of Functioning, Disability and Health (ICF) terminology and consits of three nested circles, the inner «interaction space», the intermediate «transfer phase» and the outer «real world». As represented schematically on this slide, two primary factors within the «interaction space» influence the nature of the interaction between the user and the virtual environment. These include demographic factors (e.g. age, gender, cultural background), body functions (e.g. cognitive, sensory, motor) and structures (e.g. arms, legs). The second factor relates to characteristics of the virtual environment including both the type of VR platform and ist underlaying technology (enabling the flow of information to and from the user) and the nature and demands of the task to be performed within the virtual environment. The characteristics of the virtual environment may be either barriers or enablers to performance. The patient interacts within the virtual environment, performing functional or game-like tasks of varying levels and difficulty. This enables the therapist to determine the optimal environmental factors for the patient. Within the «interaction space» sensations and perceptions related to the virtual experience take place: here the patient’s sense of presence is established, and the process of assigning meaning to the virtual experience and the actual performance of virtual tasks or activities occur.
From the interaction space (inner circle) we move to the transfer phase (intermediate circle) since our goal in rehabilitation is to improve daily function in the real world and this requires transfer of trained skills or tasks as well as environmental modifications from the virtual environment to the real world. The «transfer phase» may be very rapid and accomplished entirely by the patient or may take time and need considerable guidance and mediation from the clinician. Finally, the large, outer circle represents real world environments illustrating that the ultimate goal is to help the patient achieve participation in the real world environment by overcoming, adapting to or minimizing the environmental barriers. The entire process is facilitated by the clinician whose expertise helps to actualize the potential of VR as a rehabilitation tool.
Kizony R, Katz N, Weiss PL (2004) Virtual reality based intervention in rehabilitation: relationship between motor and cognitive abilities and performance within virtual environments for patients with stroke. Proc 5th Int Conf Disability, Virtual Reality and Assoc. Tech. Oxford, UK

## Slide 51: Realidad virtual: Elementos
Componentes hardware
Input primario usuario (Teclado, ratón, Joystick/3D, dispositivos para apuntar (con la mano o todo el cuerpo)
Interfaz de seguimiento (cabeza, cuerpo, mano o el ojo)
Interfaz háptica, visual, auditive.
Componentes de software
Procesos input
Procesos simulación
Proceso de renderizado
Base de datos
Componentes software
Componentes hardware

## Slide 52: Realidad virtual: Hardware
  Casco o mascara que proporciona un estímulo visual o auditivo
  LCD o CRT para imágenes estéreo
  Opciones de seguimiento de cabeza y cascos estéreo.
Head-Mounted Display (HMD)
  Dispositivo esteroscópico acoplado a la cabeza
  CRT para alta resolución
  Seguimiento de movimientos integrado
  Proyección de imágenes estéreo en un habitáculo en cubo.
  El seguimiento de la cabeza ajusta la proyección a la posición de la persona
Binocular Omni-Orientation Monitor (BOOM)
Cave Automatic Virtual Environment (CAVE)
  Sensores de seguimiento de la posición y orientación de los dedos.
  Permite una interacción natural con objetos
Data Glove
Control Devices
  Control virtual de objetos en 3D (Joystick, ratón)
Notes: Kiper lecture
Used hardware:
- Head-Mounted Display (HMD)
A Helmet or a face mask providing the visual and auditory displays. Use LCD or CRT to display stereo images. May include built-in head-tracker and stereo headphones
http://www.geeky-gadgets.com/carl-zeiss-cinemizer-3d-oled-head-mounted-display-finally-starts-shipping-16-10-2012/
- Binocular Omni-Orientation Monitor (BOOM)
Head-coupled stereoscopic display device. Uses CRT to provide high-resolution display. Convenient to use. Fast and accurate built-in tracking.
http://www.macs.hw.ac.uk/~hamish/9ig2/topic22.html
- Cave Automatic Virtual Environment (CAVE)
Provides the illusion of immersion by projecting stereo images on the walls and floor of a room-sized cube. A head tracking system continuously adjust the stereo projection to the current position of the leading viewer.
http://www.jvrb.org/past-issues/3.2006/589/view?set_language=de
- Data Glove
Outfitted with sensors on the fingers as well as an overall position/orientation tracking equipment. Enables natural interaction with virtual objects by hand gesture recognition.
http://i-am-fast.com/virtualreality.aspx
- Control Devices
Control virtual objects in 3 dimensions.
http://www.theverge.com/2013/12/23/5238118/virtual-reality-check-oculus-rift-hardware-ecosystem
Mirror arm display without motion sickness
Pescatore et al. (2008), Presence 2008

## Slide 53: Realidad virtual: Campos de aplicación
Diseño, ingeniería, marketing y fabricación
Medicina y cuidado de la salud
Operaciones peligrosas en entornos extremos u hostiles
Capacitación en operación de maquinaria militar e industrial, enseñanza médica y planificación / capacitación quirúrgica.
Notes: Lucca LF, Canelieri A, Pignolo L (2010) Application of virtual reality in neurorehabilitation: an overview, Virtual Reality, Prof. Jae-Jin Kim (Ed.), ISBN: 978-953-307-518-1, InTech

## Slide 54: Realidad virtual: Dispositivos
Movimiento de todo el cuerpo
No inmersivos
Inmersivos
Sin movimiento de todo el cuerpo
Captura del movimiento por sensores
Captura del movimiento por cámara / video
Interacción con joystick, teclado o ratón
Específicos rehabilitación
Específicos de rehabilitación disponibles comercialmente
Específicos de rehabilitación disponibles comercialmente
Específicos de rehabilitación disponibles comercialmente
Monitor montado en cabeza Guantes feedback
Cámara detecta los movimientos del cuerpo de la persona
Sensores de movimiento detectan el movimiento del aparato (control remoto o guante)o el movimiento del usuario en el sistema (plataforma, robot)
Joystick, teclado o ratón
Totalmente inmersivos, vista en primera persona
Relfejo de la imagen en espejo
El usuario es representado como un avatar: vista en primera o 3 persona
El usuario es representado como un avatar: vista en primera o 3 persona
Notes: How can virtual reality systems be classified?
Virtual reality systems can be classified by describing how users interact with the virtual environment and how users are represented within the virtual environment. Slide outlines the characteristics of these different categories and provides examples.
1. Immersive virtual reality:
In this type of virtual reality, the user wears a head-mounted display such that they are immersed in a first-person view of a three-dimensional virtual environment. Their view of the virtual world is controlled through head movements. The virtual environment is seen at full-scale (Chau, 2009). Immersive virtual reality systems require substantial hardware and software. For example, this type of virtual reality may also incorporate the use of force feedback gloves that allow users to sense their interaction with virtual objects (Chau, 2009). These systems can be very expensive and are generally limited to research laboratory use.
2. Non-immersive virtual reality:
This type of virtual reality refers to all systems that do not involve the use of head-mounted displays to control the user's view of the virtual environment. Instead, users view the virtual environment on a two-dimensional flat screen, and interact with it through a variety of motion-detecting interfaces.
2.1 Systems that involve total-body movement
a. Motion-capture, camera/video-based virtual reality: The user interacts with the virtual environment through body movements alone. Motion-capture virtual reality systems involve the use of a camera to capture the users' body movements. The user's image is seen in mirror-image view within the virtual or actual environment on a two-dimensional screen (Weiss et al., 2004). The screen also displays virtual objects with which the user can interact. There are both rehabilitation-specific and commercially-available examples of these types of systems.
Motion-capture, sensor-based virtual reality: The user interacts with the virtual environment using a sensor interface (e.g. remote, platform, robot, or glove). In this type of virtual reality, interaction with the virtual environment is through a type of sensor interface that the user holds, wears, or stands upon. The user is represented as an avatar within the virtual environment or is invisible within the virtual environment. There are both rehabilitation-specific and commercially-available examples of these types of systems.
2.2 Systems that do not involve total-body movement:
Computer games: Interaction with the virtual environment is via a mouse, joystick, keyboard or other device. This type of virtual reality system involves upper extremity movement to manipulate a keyboard, mouse, joystick or other device. In addition to promoting upper extremity skills, these systems can be used to improve visual-spatial planning, spatial orientation, co-ordination or memory skills. The user is invisible or is represented as an avatar within the virtual environment.
Levac D, Missiuna C (2009) AN UPDATE ON THE USE OF VIRTUAL REALITY TECHNOLOGY TO IMPROVE MOVEMENT IN CHILDREN WITH PHYSICAL IMPAIRMENTS
http://www.canchild.ca/en/canchildresources/VirtualRealityTechnology.asp

## Slide 55: Realidad virtual: Dispositivos inmersivos
Vista en primera persona de un mundo 3d virtual
El Usuario lleva normalmente gafas
Sensación de presencia
Las escenas virtuales responden a las acciones del sujeto
“El objetivo de la realidad virtual inmersiva es que el Usuario se meta completamente dentro del mundo generado por el ordenador.”
Furht 2008, Encyclopedia of Multimedia
Notes: http://link.springer.com/referenceworkentry/10.1007%2F978-0-387-78414-4_85

## Slide 56: Realidad virtual: Dispositivos no inmersivos
Uso del monitor para proyectar el mundo virtual.
Interacción a través de los sensores de movimiento.
Los sujetos responden totalmente en el entorno real.
“El Sistema de realidad virtual a menudo consiste en un monitor de ordenador, un ratón, un teclado, joystick, dispositivos hápticos y sensors de fuerza.”
Ortiz-Catalan et al., 2014
Notes: Ortiz-Catalan M, Nijenhuis S, Ambrosch K, Bovend’Eerdt T, Koenig S, Lange B (2014) Virtual Reality in JL Pons & D Torricelli, Emerging Therapies in Neurorehabilitation, Biosystems & Biorobotics.

## Slide 57: Realidad virtual: Ventajas
Ventajas
Entrenamiento intensive (repeticiones) y aumento de la motivación con mayor feedback
Mejora de la eficacia y resultados al hacer las tareas más sencillas, menos demandantes y menos tediosas
Los entornos de realidad virtual son flexibles y adaptables a diferentes Objetivos terapeúticos
Notes: Ortiz-Catalan M, Nijenhuis S, Ambrosch K, Bovend’Eerdt T, Koenig S, Lange B (2014) Virtual Reality in JL Pons & D Torricelli, Emerging Therapies in Neurorehabilitation, Biosystems & Biorobotics.
  VR also provides the capacity to individualize the complexity of tasks and decreasing the support provided by the clinician
Schultheis MT, Rizzo AA (2001) The application of virtual reality technology for rehabilitation. Rehabilitation Psychology 46: 296-311
  Motivated patients would be encouraged to practice movements in a repetitive manner thereby improving their condition, an achievement that is not easy to attain via conventional therapy
Liepert J, Baunder H, Wolfgang HR, Miltner WH, Taub E, weiller C (2000) Treatment-induced cortical reorganization after stroke in humans. Stroke 31: 1210-1216
What are the potential benefits of virtual reality technology?
The use of virtual reality systems may:
· Allow for repeated and consistent practice of the same task (Rizzo & Kim, 2005; Rose, Brooks, & Rizzo, 2005)
· Enable clinicians to progress difficulty and challenge levels (Rizzo & Kim, 2005)
· Enable clinicians and researchers to easily record and analyze performance outcomes (Rizzo & Kim, 2005)
· Provide a safe environment to undertake tasks which may be difficult or unsafe in real life (e.g crossing a street, operating a motorized wheelchair) (Rizzo & Kim, 2005; Schultheis & Rizzo, 2001)
· Offer appealing games that may make therapy tasks more fun and engaging, which may increase compliance with therapy (Rizzo & Kim, 2005)
· Enhance motivation to practice which may lead to longer practice duration or more practice repetitions (Harris & Reid, 2005; Rizzo & Kim, 2005)
· Provide enhanced real-time feedback about task performance or task results which may be beneficial for learning (Holden, 2005; Rizzo & Kim, 2005)
· Be useful as home interventions involving independent practice (Rizzo, Strickland, & Bouchard, 2004)
· Provide potential for telerehabilitation, if the virtual reality system is internet-deliverable (as clinicians can monitor clients' practice from afar) (Huber et al., 2008; Rizzo et al., 2004)

## Slide 58: Realidad virtual: Limitaciones
Limitaciones
Falta de estándares, marcos de trabajo y compatibilidad
Mareos, dolor de cabeza, cyber sickness
Aspectos legales: registro como aparatos médicos
Coste Elevado de los sistemas plenamente inmersivos
Notes: Ortiz-Catalan M, Nijenhuis S, Ambrosch K, Bovend’Eerdt T, Koenig S, Lange B (2014) Virtual Reality in JL Pons & D Torricelli, Emerging Therapies in Neurorehabilitation, Biosystems & Biorobotics.
Crosbie JH, Lennon S, McGoldrick MC, McNeill MDJ, McDonough SM (2012) Virtual reality in the rehabilitation of the arm after hemiplegic stroke: a randomized pilot study. Clin Rehanil 26(9): 1088-1097
Rizzo A, Kim GJ (2005) A SWOT analysis of the field of virtual reality rehabilitation and therapy. Presence 14(2): 119-146

## Slide 59: Linkage to Neural Principles and Learning
Feedback
Learning process must be reinforced by feedback
Feedback links patient’s performance to successful task outcome
Repetitions
Motivation
Motivation is needed to repetitively carry out task
Repetitions are important to promote motor learning and cortical plasticity
+
=
Increasing difficulty
Increasing skills
Too hard
Too easy
Ideally difficulty progression
Notes: VR offers a realistic, safe and motivational setting in which complex activities can be practiced. In an overview of VR technology by Rizzo and Kim (2005) motivating game factors are described as one of the major advantages of VR systems, especially as a part of clinical assessments. When patients are engaged in gaming tasks, attention is drawn away from the fact that an assessment is taking place, thus providing a more accurate estimate of naturalistic capability. Further evidence suggests that when a user concentrates on the game rather than their impairment, exercises becomes more enjoyable, motivating and more likely to be maintained over the many trials needed to induce plastic changes in the nervous system. Feedback can be very important for the user’s motivation. The user always needs to know when and why a task was completed (un-) successfully in order to promote (errorless) learning and prevent frustration. Feedback can be given as absolute (correct/incorrect) or graded information (error scores, deviation from optimum) and in different modalities. Most computer application and VR systems present the user with visual and auditory information.
Motor rehabilitation should be focused on functional movements in a relevant environment with high intensity, a large number of repetitions and appropriate feedback (Timmermanns et al. 2009)
http://lermagazine.com/issues/january/fighting-falls-with-feedbac-virtual-reality-training-improves-balance

## Slide 60: eStimulación cerebral
6

## Slide 61: Estimulación cerebral
En el siglo I, un medico romano, Scribonius Largus aplicaba Corrientes eléctricas a través del pez torpedo a sus pacientes para tartar los dolores de cabeza.
La investigación científica surge de la electroterapia en los inicios del siglo 19.
Potencial para tratar la depression, dolor crónico, acelerar la recuperación del ictus, etc.
La estimulacion cerebral es una técnica que aplica de forma directa (electrodos) o indirecta (bobina magnética) una estimulacion eléctrica a una población de neuronas del cerebro
Adaptado de Wikipedia
Concepto:
electricidad
Estimulación cerebral
+
=
cerebro
Notes: Understanding effect of stimulated neuron populations is the big challenge.
Hummel and Cohen 2006
Patients with stroke experience changes in motor cortical excitability [8–11] and an abnormally high interhemispheric inhibition from M1 intact hemisphere to M1 lesioned hemisphere with movements of the paretic hand that is more prominent in cases with more substantial motor impairment. [1] These findings, consistent with interhemispheric competition models of sensory and motor processing, [12–15] raised the hypothesis that purposeful modulation of excitability in motor regions of the intact and affected hemisphere may contribute to improvements in motor function. [16]
Emerging therapies in neurorehabilitation
Changes in the sensory and motor maps usually characterize several disorders that involve motor and sensory disturbances. There are a lot of studies in the literature that have investigated the possibility of rehabilitation inducing plastic reorganization of brain lesion. The use of brain stimulation in rehabilitation is characterized by the ability of the reorganization of surviving neural circuits after cortex damage. Recovery is achieved by combining motor function training with stimulation training. Training would lead to a redistribution of representations to undamaged areas of the sensory cortex via reorganization (Flor and Diers 2009). Therefore, motor learning, or relearning, is fundamental to neurological rehabilitation. To improve motor performance during learning, we use an iterative process, repeating voluntary movements and identifying and correcting errors. Recovery means that undamaged brain regions are recruited, which generate commands to the same muscles as were used before the injury’’ (Krakauer 2006).
This knowledge is used to develop new rehabilitation treatments. For instance, in sensorimotor rehabilitation, the primary intention would be to stimulate the sensorimotor cortex, in order to induce a plastic reorganization. There are 2 different ways to induce a plastic reorganization:
• Indirect (‘‘passive brain stimulation’’) stimulation through sensorial feedback for the aim of inducing motor relearning.
• Direct (‘‘active brain stimulation’’) stimulation intended to influence and eventually to change electrical neural activity
Sensory and motor functions are intimately correlated in motor skills but not in reflex motor or automatic movements. Somatosensory information and feedback can modify the on-going motor behavior, triggering preprogrammed corrective action. Additionally, it was shown that animals with damage to the primary motor cortex would increase their dependency on visual monitoring of reaching, reinforcing the interrelationship of sensory processing and motor control (Nudo et al. 2000). This reinforcement occurs because the motor cortex and the sensory cortex are found side by side in the parietal lobes of the brain. For this reason, a damaged brain area could be trained, during session therapy, by visual, auditory, or tactile sensory stimulation (indirect stimulation); see (Flor and Diers 2009). For instance, patients with phantom limb pain provided evidence that providing the impression of viewing one intact hand in a mirror instead of the amputated hand leads to better movement and less pain in the phantom limb (Ramachandran et al. 1995).
Image (modulation)
http://brainmodulation.com/wp-content/uploads/2014/06/brain-mod-assfn.jpg

## Slide 62: Estimulación cerebral: Elementos
Estimulador
Determina la frecuencia, intensidad y longitud de la estimulación
Electrodos o bobina magnética
Aplica un voltaje sobre la piel o un campo magnético
Fuente de alimentación
Proporciona electricidad para dar la estimulación
estimulador
electrodos
Bobina magnética
Fuente de alimentación
o

## Slide 63: Estimulación cerebral: Métodos
Estimulación magnética transcraneal (TMS)
Estimulación transcraneal de corriente directa
(tDCS)
Estimulación cerebral profunda
(DBS)
No invasiva
Invasiva
Bobina magnética &
Campo magnético
Electrodos y corriente
Electrodos y corriente
Notes: Some stimulation therapies that aim for brain regions directly are transcranial magnetic stimulation (TMS), transcranial direct current stimulation (tDCS), and
deep-brain stimulation (DBS). They are used principally to treat brain diseases or improve functional deficits, as in depression, Parkinson disease, epilepsy, and dystonia (for a review, see: (Wassermann and Lisanby 2001)). rTMS and tDCS are noninvasive procedures. tDCS uses constant, low current delivered directly to the brain area of interest via small electrodes. tDCS was originally developed to help patients with stroke. Their main advantage is the hope for noninvasive, drug-free treatment. Instead, DBS is a treatment that needs a surgical procedure. It consists of an implanted device, which sends electrical signals to brain areas regulating brain activity.
TMS is a subset of electrotypes and used to stimulate the primary motor brain cortex for assessing excitability that is associated with motor relearning and
improvement of motor function (Barbay and Nudo 2009). Navigated TMS utilizes individual magnetic resonance images for accurate localization of stimuli; this feature is specifically useful when repeated measurements are performed. Thus, repeatable stimuli can be applied to a certain location; plus, coil orientation and tilting can be controlled. A descendant of TMS, repetitive TMS (rTMS), has been investigated in a variety of neurological conditions and psychiatric disorders, including addictions, depression, and auditory hallucinations. Writer’s cramp, or focal hand dystonia, is characterized by involuntary coactivation of an antagonist.
(Murase et al. 2005) used subthreshold low-frequency (0.2 Hz) rTMS, which exerted an inhibitory action on the cortex. They found that stimulation of the
premotor cortex, but not the motor cortex, significantly improved the rating of handwriting. Tests demonstrated that tDCS could increase cognitive processes on a variety of tasks. An example is shown in (Reis et al. 2009); they used tDCS over the primary motor cortex during learning of a novel motor skill task. Their aim was to find strategies that enhanced skill acquisition or retention. They analyzed the stimulation effect on both within-day and between-day effects and on the rate of forgetting during a 3-month follow-up. Amazingly, they found that tDCS, across the 3-month follow-up period, had favored a consolidation mechanism. This may hold promise for the rehabilitation of brain injuries. Nowadays, at the point at which research has arrived, we can think of rTMS and tDCS as helpful tools in rehabilitation therapy; instead, DBS seems to promise, in the future, permanent or longer-term usage.
In this chapter, we discuss the use of noninvasive
brain stimulation (NIBS) in the setting of stroke rehabilitation.
Interest in NIBS developed after the observation
of long-term effects on cortical excitability that
occur after repeated stimulation (Huang et al., 2005;
Fitzgerald et al., 2006; Nitsche et al., 2008). Depending
on the stimulation parameters, motor cortical excitability
can be reduced (inhibition) by means of low-frequency
repetitive TMS (rTMS), continuous theta-burst stimulation
(cTBS), and cathodal tDCS, or enhanced (facilitation)
by means of high-frequency rTMS, intermittent thetaburst
stimulation (iTBS), and anodal stimulation. There
is evidence that links the effects of these NIBS techniques
to long-term potentiation (LTP)-like and long-term
depression (LTD)-like mechanisms (Cooke and Bliss,
2006; Thickbroom, 2007; Wagner et al., 2007; Ziemann
et al., 2008; Fritsch et al., 2010). After stroke, NIBS has
been studied as a tool to modulate cortical excitability
in the affected and intact hemispheres, predominantly with the goal of correcting hypothesized imbalances
in interhemispheric interactions (Kinsbourne, 1974;
Hummel and Cohen, 2006).
Bihemispheric reorganization
Longitudinal neuroimaging studies have shown initially
high bihemispheric BOLD signal activity associated with
movements of the paretic hand 2 weeks poststroke. Over
time, bihemispheric activation decreases progressively
toward levels observed in healthy subjects concomitant
to motor recovery (Ward et al., 2003; Tombari et al.,
2004; Rehme et al., 2011). In opposition to this pattern,
patients with incomplete motor functional recovery in
the chronic phase (i.e., more than 6–12 months poststroke)
typically maintain increased bihemispheric
BOLD signal activity (Chollet et al., 1991; Weiller et al., 1992; Ward and Cohen, 2004; Gerloff et al., 2006;
Grefkes et al., 2008b). Consistent with these findings, it
has been reported that lateralized fMRI activation
towards ipsilesional regions, similar to that seen in
age-matched controls, is associated with more successful
functional recovery (Ward et al., 2003; Gerloff
et al., 2006; Nair et al., 2007).
Studies using TMS have attempted to discern the
functional role of these neuroimaging findings. It is
now known that the presence of ipsilateral MEPs to
TMS applied over the contralesional M1 is associated
with poor clinical outcome (Turton et al., 1996; Netz
et al., 1997; Feydy et al., 2002). In addition to M1,
TMS applied to the contralesional dorsal PMC in poorly
recovered patients disrupted motor performance of the
paretic hand (Johansen-Berg et al., 2002). A neuroimaging
study carried out during the first 2 weeks after stroke
also showed that functional recovery in severely
affected patients was associated with gradually increasing
activity in contralesional M1 and PMC (Rehme et al.,
2011). In line with this, Lotze and colleagues (2006)
showed that disruption of activity in contralesional
regions (i.e., M1, dorsal PMC, and superior parietal lobe,
SPL) active during movements of the paretic hand
affected motor performance. While interference with
the dorsal PMC and M1 induced timing errors only,
SPL stimulation caused both timing and accuracy
deficits.
Overall, these results are consistent with the view that
patients with more severe motor impairments may
engage more actively regions of the contralesional hemisphere
to carry out a task with the paretic hand
(Johansen-Berg et al., 2002; Ward et al., 2003; Fridman
et al., 2004; Buch et al., 2012). It is possible to study physiological features of cortical
organization after stroke using TMS. Paired-pulse
TMS delivered through the same magnetic coil over
M1, where a suprathreshold test stimulus (TS) is preceded
by a subthreshold or suprathreshold conditioning
stimulus (CS), can be used to gain insight into the relative
contribution of local inhibitory and excitatory inputs
to M1 pyramidal tract cells (Reis et al., 2008). Interstimulus
intervals of approximately 1–5 ms cause attenuation
of MEP amplitudes or short intracortical
inhibition (SICI) (Kujirai et al., 1993), whereas longer
intervals (6–10 ms) elicit a facilitatory effect referred
to as intracortical facilitation. Decreased SICI has been
reported in both affected and unaffected hemispheres
of chronic stroke patients (Liepert et al., 2000a, b;
Butefisch et al., 2003, 2008). It is not only resting SICI that is abnormal after stroke, but also movement-related
SICI. For example, in stroke patients who exhibit relatively
good functional recovery, SICI measured immediately
preceding performance of a voluntary movement
by the paretic hand was abnormal compared with that
in age-matched controls (Hummel et al., 2009).
TMS has been also used to study interhemispheric
interactions. Early studies in stroke patients examined
the excitability of bilateral motor cortices evaluated by
differences in MEP amplitudes and in cortical areas
(motor maps) producing MEPs in the contralateral hand
muscles (Cicinelli et al., 1997; Traversa et al., 1997).
These investigations found relative hyperexcitability of
the contralesional in comparison with the ipsilesional
M1 that normalized with time after stroke. A pairedpulse
TMS technique has been used to study interhemispheric
inhibition (IHI) between the two M1s, where a
suprathreshold CS is applied over the conditioning M1
about 10 ms prior to the TS applied to the opposite conditioned
M1 (Ferbert et al., 1992). Abnormalities in resting
IHI after stroke may depend on the location of the
lesion (Boroojerdi et al., 1996). Other studies started to
evaluate movement-related changes in IHI after stroke.
In relatively well recovered chronic stroke patients, initially
normal levels of IHI from the contralesional to
the ipsilesional M1 remain present at the onset of a
paretic hand movement, in contrast to the disinhibition
that accompanies nonparetic hand movement and
motions in age-matched controls (Murase et al., 2004;
Duque et al., 2005).
It is also important to consider the interactions
between IHI and SICI. Examining whether changes in
IHI and SICI after stroke may be related, Butefisch
and coworkers (2008) showed that the attenuation of
SICI in ipsilesional M1 was not accompanied by a change
in resting IHI from contralesional to ipsilesional M1. In
contrast, disinhibition of contralesional M1 was accompanied
but did not correlate with a decrease in IHI from
ipsilesional to contralesional M1s. Altogether these findings
were interpreted as indicating that, at rest, local
modulation of inhibition within ipsilesional M1 is prominent.
However, a more accurate investigation of the
resting interactions between SICI and IHI using TMS
paired-pulse techniques, as recently implemented in
healthy individuals (Daskalakis et al., 2002; Perez and
Cohen, 2008), remains to be done after stroke. Additionally,
an understanding of IHI–SICI interactions in the
process of generation of a voluntary movement by the
paretic hand will be important to determine the mechanisms
underlying deficits in motor function after stroke.
For example, the phenomenon of facilitation of M1
excitability by ipsilateral limb movement has been
explored in the healthy brain (Muellbacher et al., 2000;
Hortobagyi et al., 2003; Perez and Cohen, 2008), but remains to be evaluated thoroughly after stroke. It has
been proposed that, with isometric force production,
nonparetic arm activity in stroke patients does not lead
to as much ipsilateral M1 facilitation as seen in healthy
controls (Woldag et al., 2004; Renner et al., 2005).
Overall, these findings suggest that motor function
of the paretic hand may be influenced by abnormalities
in interhemispheric inhibitory interactions. This view has
been documented extensively in recent literature using
TMS measures in healthy subjects (Tinazzi and
Zanette, 1998; Schambra et al., 2003; Kim et al., 2004;
Kobayashi et al., 2004, 2009; Dafotakis et al., 2008;
Dimyan and Cohen, 2010; Williams et al., 2010) and
fMRI (Grefkes et al., 2008a, b; Wang et al., 2010). It
was shown that stroke patients experience an increased
inhibitory influence from contralesional to ipsilesional
M1, which is not present in healthy subjects or when
the same patients moved their unaffected hand. Importantly,
the strength of this inhibition from contralesional
M1 correlated with the motor impairment of the paretic
hand (Grefkes et al., 2008b). Similar abnormalities in
interhemispheric interactions relating to other cognitive
functions have been reported in the fields of language
and spatial attention (Kinsbourne, 1980; Chrysikou and
Hamilton, 2011; Oliveri, 2011).
NONINVASIVE BRAIN STIMULATION IN
NEUROREHABILITATION
Based on the hypothesis of abnormal interhemispheric
inhibitory interactions after stroke, two strategies have
been proposed to ameliorate paretic hand function: (1)
to downregulate excitability of contralesional M1, and (2) to upregulate excitability of ipsilesional M1 (Hummel
and Cohen, 2006; Webster et al., 2006) (Fig. 40.1).Depending
on the stimulus type and stimulation parameters, NIBS
can facilitate cortical excitability in the ipsilesional M1
through direct stimulation of this region or indirectly via
inhibition of the contralesional M1. To target simultaneously
both components of this imbalance, it is possible
to use bihemispheric modulatory approaches (Takeuchi
et al., 2009; Lindenberg et al., 2010b).
Studies investigating the effects of NIBS on motor
function after stroke are summarized in Table 40.1. Emara et al., 2010; Kakuda et al., 2010a, b, 2012;
Nair et al., 2011; Avenanti et al., 2012), produces
lasting effects on hand motor function. Some of these
studies reported improvements maintained for up to
1–2 weeks (Fregni et al., 2006; Boggio et al., 2007;
Takeuchi et al., 2008), 1 month (Conforto et al., 2012;
Kakuda et al., 2012), and 3 months (Khedr et al., 2009;
Emara et al., 2010) after the end of interventions. In
one report, however, Talelli and colleagues (2007) did
not find beneficial effects of application of cTBS. Direct
comparison between these individual trials has been
difficult due to substantial differences in stimulation
protocols, endpoint measures, and the relationship of
stimulation with rehabilitative treatments and environments,
as well as patient characteristics.
In summary, there is an increasing body of literature on
possible beneficial effects of modulation of cortical
excitability in the ipsilesional or contralesional M1s, or
a combination of both on motor function. These effects
have so far been stronger when NIBS is applied in close
relationship with motor training (Takeuchi et al., 2008,
2009; Chang et al., 2010; Koganemaru et al., 2010;
Lindenberg et al., 2010b, 2012b; Bolognini et al., 2011;
Avenanti et al., 2012). The benefit of coupling NIBS with
physical practice may rely on Hebbian principles of synaptic
plasticity (Buonomano and Merzenich, 1998).
Moreover, data suggest that the effects of facilitation
or inhibition of ipsilesional or contralesional M1, respectively,
may relate not only to modulation of local
changes in cortical excitability, but also to the induction
of reorganization in distributed neural networks.
To date, no significant adverse effects have been
reported in stroke patients, such as induction of an epileptic
seizure. Thus, rTMS and tDCS appear to be safe
techniques when used according to current safety guidelines
regarding intensity, frequency, and duration of
stimulation (Poreisz et al., 2007; Rossi et al., 2009).
Well designed studies (i.e., multicenter, longitudinal,
sham-controlled) are needed to determine how effective
these techniques are in motor rehabilitation after stroke.
It is likely that the outcome of NIBS interventional
approaches may be influenced by fluctuations in resting
brain activity before or after stimulation, by homeostatic
plasticity, as conceptualized by the Binenstock–Cooper–
Monroe theory (Bienenstock et al., 1982; Ziemann et al.,
2004), and by the specific timing between rehabilitative
therapy and cortical stimulation (Avenanti et al., 2012).
Additionally, state dependency (i.e., a targeted region’s
varying response to stimulation based on its previous
state of activity) should be studied in the context of combination
of rehabilitation with stimulation (Silvanto
et al., 2008). In the future, it is possible that specific markers will
be developed to help identify patients who can benefit
the most from NIBS interventions based on individual
patterns of cortical activation (Nowak et al., 2008;
Ameli et al., 2009), white-matter microstructural integrity
(Stinear et al., 2007; Lindenberg et al., 2012a), or
presence of certain genetic polymorphisms (Kleim
et al., 2006; Cheeran et al., 2009b; Fritsch et al., 2010).

## Slide 64: Estimulación cerebral: EMT
Una técnica no invasive que consiste en un campo magnético que emana de una bobina que se coloca sobre la cabeza. El campo magnético induce una corriente eléctrica en las regions del cerebro cercanas al punto de estimulación.
MedicineNet.com
Figure 2. Schematic representation of how to assess brain plasticity with TMS. As recorded using either electromyography (EMG) or electroencephalography (EEG), brain responses to TMS can be measured as motor evoked potentials (when TMS is applied to motor cortex) or localized evoked field potentials. Comparison of these TMS-based measures of cortical reactivity before and after a given intervention (e.g., PAS, rTMS, TBS, task) can provide an index of brain plasticity in response to that intervention.
Principio:
Activa o suprime la actividad en regions corticales.
El efecto de la EMTr dura hasta horas después del período de estimulación
Permite un mapeo preciso de la representación de la musculatura
Útil para caracterizar lesiones del SNC
Hace que las neuronas en reposo se activen
Notes: Hummel and Cohen 2006
Transcranial magnetic stimulation (TMS)
Delivered to the brain by passing a strong brief electrical current through an insulated wired coil placed on the skull. Current generates a transient magnetic field in the brain inducing electric currents in the cortex that flow parallel to the coil and depolarize neurons. Depending on the frequency, duration of the stimulation, the shape of the coil, and the strength of the magnetic field TMS can activate or suppress activity in cortical regions. Effects of repetitive TMS can outlast the stimulation period for up to 1–2 h. [24,25]
Emerging therapies in neurorehabilitation
Transcranial magnetic stimulation (TMS) is one of the principal non-invasive techniques used to investigate functionality and interconnections of the brain. TMS is a comfortable and safe technique with well-established standard protocols (Rossini et al. 1994). TMS has been approved for pediatric application but is not recommended for children younger than 6-7 years, due to the high neural activation by evoking motorevoked potentials (MEPs) (Wittenberg 2009).
TMS generates rapidly changing magnetic field pulses to induce a weak electrical activity in focal brain areas (Hoyer and Celnik 2011). When the motor cortex receives sufficient current to produce the synchronic activation of upper and lower motor neurons, MEPs can be recorded on single or multiple muscles. Therefore, TMS allows an accurate mapping of muscle representation in the primary brain cortex and estimating of the speed/magnitude of the MEPs. From these maps, the size and location of muscles and movement cortical representations can be determined. These features can all be used to characterize characteristics (size, spreading,...) of CNS injuries (Milot and Cramer 2008). TMS-derived metrics thus relate to motor abnormalities. For example, there appears to be a relationship between the area of the motor cortex dedicated to a specific movement and the motor ability. Although the interpretation is complex, Liepert et al. associated larger motor maps with functional recovery after stroke rehabilitation (Liepert et al. 2000). In particular, TMS has been used in combination with MRI to perform early diagnosis of hand function in children with CP (Holmström et al. 2010). The time gained by incorporating TMS to standard diagnostic methods allows bringing forward the therapy and thus increases its rate of success.
Image (motor mapping)
http://www.frontiersin.org/files/Articles/31877/fnins-07-00042-HTML/image_m/fnins-07-00042-g002.jpg

## Slide 65: Estimulación cerebral: tDCS
Una técnica no invasive que utiliza una corriente constante y baja, aplicada directamente sobre el área cerebral que interesa a través de pequeños electrodos.
Adaptado de Wikipedia
Principio:
Modulación de la actividad cerebral que se puede aplicar antes o durante la práctica.
Región anódica: despolariza la membrana neuronal, haciéndola más propensa a dispararse.
Región catódica: hiperpolariza la membrana neuronal, por lo que es menos probable que se dispare.
Se cree que modula la velocidad de activación de las neuronas activas.
Notes: Hummel and Cohen 2006
tDCS (1–2 mA)
Applied through two surface electrodes placed on the skull – eg., for the primary motor cortex (M1), one electrode is placed over M1 and one other over the contralateral supraorbital region. Depending on duration and polarity of stimulation, tDCS enhances or depresses excitability in the stimulated region for minutes to 1–2 h. Does not seem to induce direct neuronal depolarization like TMS but modulates the activation of sodium and calcium-dependent channels and NMDA-receptor activity, promoting long-term-potentiation/long-term-depression-like mechanisms.
Emerging therapies in neurorehabilitation
As mentioned earlier, the manipulation of cortical excitability may have therapeutic benefits for patients with neurological impairments, and specifically for
patients with CP (Vidailhet et al. 2009; Hayek et al. 2009). In rats, increased cortical excitability has been found to enhance brain plasticity (Holt and Mikati
2011). Transcranial direct current stimulation (tDCS) has been proposed as an alternative form of non-invasive neurostimulation to promote plasticity and
modulate brain excitability. tDCS has been reported to lead to functional changes in discrete areas of the cerebral cortex by shifting membrane potential. In tDCS, low intensity currents (1–2 mA) are applied directly to the brain area of interest over a sustained period of time (5–30 min). tDCS is less focal than TMS, mainly due to the relatively large size of the electrodes used to deliver current over the scalp. However, tDCS unlike classical neurostimulation methods, does not produce muscle fasciculation that can be uncomfortable and often painful for the patient (Hayek et al. 2009). Thus, tDCS-based neurostimulation sessions are likely to be more tolerable, although it does not avoid classical side effects such as headache, dizziness, nausea or itching sensation (Nitsche et al. 2008).
Similar to TMS, tDCS can also enhance excitability via anodal polarization or decrease it via cathodal polarization (Song et al. 2011). Tests on healthy adults
demonstrated that tDCS can increase cognitive performance on a variety of tasks, depending on the cortical area being stimulated (Chi and Snyder 2011). tDCS has been shown to be an effective treatment for migraines, depression or pain, but also constitutes an interesting tool for the modulation of motor cortex excitability (Nitsche and Paulus 2000). Nitsche et al. demonstrated that the application of tDCS can modulate the cortical excitability and influence spontaneous neural activity influencing synaptic function (Nitsche et al. 2008). To the best of our knowledge, there are no studies done in children with CP using tDCS. It is important to highlight that tDCS is a technique that is just starting to be tested in the clinical field, so, protocols for safety and effectiveness have not been yet to be standardized, even for adults (Nitsche et al. 2008).

## Slide 66: TMS vs. tDCS
Estimulación magnética transcraneal
TMS
Estimulación transcraneal de corriente directa
tDCS
  Efecto dura horas.
  En general coste menor.
  Bajo riesgo de problemas secundarios.
  Buena condición placebo.
  Pobre resolución especial y temporal.
  Modulación simultánea del área cerebral bajo el electrodo de referencia.
  Protocolos menos establecidos.
  Puede provocar dolores de cabeza transitorios.
  Efecto dura varias horas
  Buena resolución especial y temporal (ms)
  Protocolos bien establecidos
  Precio elevado
  Riesgo de crisis comiciales (raro)
  Limitado a áreas superficiales cerebrales.
  Puede provocar dolores de cabeza transitorios.
  No buenas condiciones placebo.
Notes: Hummel and Cohen 2006
Similarities
Similar duration of effects (up to hours), non-invasive, and deemed to be safe (adhering to guidelines=
Differences
Possible mechanisms underlying their effects; TMS equipment is more expensive, allows more focal stimulation, protocols are better established; TMS applied with millisecond level accuracy whereas tDCS is applied over minutes tDCS is easier to use in double-blind or sham-controlled studies, and more easily applied simultaneous to cognitive and motor training protocols
Safety
rTMS can cause seizures, but strict rules of use and training protocols have made them rare [36]. Patients with a history of seizures should be excluded from studies using this technique. Safety studies are needed for tDCS; brief tingling sensations are common, rarely accompanied by redness under the electrodes [27,35,38]. Transient headaches have been described for both interventions
Remote effects
Application of both of these techniques to one cortical region will probably influence distant cortical or subcortical sites through trans-synaptic effects
In patients with brain lesions, expected models of current flow elicited by both of these techniques may differ from those in healthy brains [37].
Non-specific effects on attention, fatigue, discomfort, or mood
Specificity of both of these techniques on cognitive or motor measures may be influenced by possible concomitant effects on attention, fatigue, discomfort, or mood
Study design and experimental hypotheses
Given these characteristics, similarities, and differences the choice of technique to modulate cortical function is highly dependent on study design and experimental hypotheses
Handbook of clinical neurology
tDCS
Pro: Painless. Reliable sham condition with no scalp sensations. Low risk of adverse effects and seizure induction. Modulates neuronal activity during execution of a specific task. Low cost-
Contra: Poor spatial and temporal resolution. Stimulation of large part of the brain. Concurrent modulation of area under reference electrode
rTMS
Pro: Good spatial and temporal resolution. It covers a larger time window (versus spTMS), allowing evaluation of the online involvement of the stimulated area. It modulates neuronal activity during the execution of a specific task. Short- and longterm Neuromodulatory effects
Contra: High cost. Limitations to stimulation of superficial areas of the brain. Possible undesired shortand long-term Neuromodulatory effects. Noisy. Can induce involuntary muscle movements. No good sham condition. Safety concerns

## Slide 67: Contacto
International Industry Society in Advanced Rehabilitation Technology (IISART)
General Information
info@iisartonline.org www.iisartonline.org
Centro Europeo de Neurociencias CEN
info@eneurocenter.com
www.eneurocenter.com

## Slide 68: Bibliografía
[1] Poli et al. 2013, Robotic Technologies and Rehabilitation: New Tools for Stroke Patients’ Therapy.
[2] Diaz et al. 2011, Lower-Limb Robotic Rehabilitation: Literature Review and Challenges.

## Slide 69: Fuentes de imágenes
Slide 2 – Audience Background: http://www.iisd.ca/ymb/climate/wcc3/pix/1sept/DSC_6266%20full%20room.jpg
Slide 3 – Reasons for New Technologies Left: http://www.unece.org/typo3temp/pics/8346dcaa95.jpg Middle (upper): http://emergingtech.tbr.edu/sites/default/files/styles/flexslider_full/public/NewTech_0.jpg?itok=WghHlgJO Middle (lower): http://timpexelectronics.com/wp-content/uploads/2014/03/Electronics-0000166421891-1100x732.jpg Right: http://www.nature.com/sc/journal/v41/n12/fig_tab/3101518f1.html
Slide 4 – Usage of New Technologies 1st image (motor learning): http://www.vi-hotels.com/typo3temp/pics/s_1ad5acb5b7.jpg 2ndimage (brain injury): http://www.eusi.org/wp-content/uploads/2012/11/stroke.jpg 3rd image (therapy): Hocoma 4th image (assessments): http://www.hopkinsmedicine.org/healthlibrary/GetImage.aspx?ImageId=268329 5th image (daily activities): http://static.guim.co.uk/sys-images/Guardian/Pix/pictures/2013/10/28/1382979259350/Gardening-and-DIY-can-pro-011.jpg
Slide 9 – Rehabilitation Robotics Light bulb: http://theosophy.net/forum/topics/theosophists-and-the-light Robot: http://bsiswoyo.lecture.ub.ac.id/files/2011/12/puma560-1.png Arm/leg orthosis: http://www.broadenedhorizons.com/powergrip-add-on-kit Therapeutic robot: From Lum et al. 2006, MIME robotic device for upper-limb neurorehabilitation in subacute stroke subjects: A follow-up study.

## Slide 70: Fuentes de imágenes
Slide 10 – Robotic Therapy: Elements Image (Lokomat): Hocoma
Slide 11 – Robotic Therapy: Devices 1st image (Lopes): http://www.blogcdn.com/www.engadget.com/media/2011/02/lopesexoskeletontwente-1298501841.jpg 2nd image (Armeo Power): Hocoma 3rd image (InMotion): http://imt.lynxdesign.com/wp-content/uploads/2012/11/HandRobotTherapy.png 4rd image (Lokomat): Hocoma 5th image (Gentle/S): http://www.reading.ac.uk/AcaDepts/si/gentle/103-0325_IMG.JPG 6th image (Mime): http://www.rehab.research.va.gov/jour/00/37/6/images/BURG-F03.JPG 7th image (G-EO System): http://www.skoutasmedical.gr/portal/components/com_virtuemart/shop_image/product/G_EO_System_Evol_4f4767f5b831c.jpg 8th image (Gait Trainer): http://www.reha-stim.de/cms/assets/images/GT-I-mit-Person 9th image (Bi-Manu-Track): http://www.reha-stim.de/cms/assets/images/Bi-Manu-Track-09.jpg 10th image (Lokohelp): http://www.woodway.de/images/productimages/LokoHelp_with_PPS.png
Slide 12 – Robotic Therapy: Exoskeletons Images: Created for slide pool
Slide 13 – Robotic Therapy: End-Effector Devices Images: Created for slide pool
Slide 14 – Exoskeletons vs. End-Effector Devices Images: Created for slide pool

## Slide 71: Fuentes de imágenes
Slide 15 – Robotic Therapy: Upper Limbs Left images (unilateral): http://imt.lynxdesign.com/wp-content/uploads/2012/11/HandRobotTherapy.png Left images (bilateral): From van Delden 2012, A Systematic Review of Bilateral Upper Limb Training Devices for Poststroke Rehabilitation. Middle images (2 Dof): From Metzger et al. 2012, High-Fidelity Rendering of Virtual Objects with the ReHapticKnob – Novel Avenues in Robot- Assisted Rehabilitation of Hand Function. Middle images (6+1 Dof): Hocoma Right images (elbow): http://nyp.org/img/enewsletters/e100_patient_balls.jpg Right images (fingers): http://tyromotion.com/wp-content/uploads/2013/02/Amadeo_1.png
Slide 16 – Robotic Therapy: Lower Limbs Treadmill: Hocoma Foot-plates: http://www.rehatechnology.com/upload/cms/user/G-EO_System_brochure_EN.pdf, page 4 Overground: http://c1.staticflickr.com/5/4083/5169846467_b25ee3cc73_n.jpg Active foot orthoses: http://www.mdpi.com/robotics/robotics-03-00120/article_deploy/html/images/robotics-03-00120-g007-1024.png
Slide 17 – Robotic Therapy: Control Strategies Images: Adapted from Teasell and Hussein 2013, Evidence-Based Review of Stroke Rehabilitation: Background Concepts in Stroke Rehabilitation
Slide 18-20 – Advantages and Limitations Icons: Created for slide pool

## Slide 72: Fuentes de imágenes
Slide 21 – Linkage to Neural Principles and Learning Left image (repetitions): Hocoma Middle image (pract. time): http://cms.birdinhand.com.au/bird/wp-content/uploads/sites/2/2014/10/hour-glass.jpg Right image (difficulty): Existing presentation
Slide 22 – Linkage to Neural Principles and Learning Left image (segmentation): Created for slide pool Middle image (motivation): Created for slide pool Right image (feedback): Existing presentation
Slide 24 – Non-Actuator Devices Light bulb: http://theosophy.net/forum/topics/theosophists-and-the-light Left image: From Lum et al. 2006, MIME robotic device for upper-limb neurorehabilitation in subacute stroke subjects: A follow-up study. Middle image (actuator): http://www.intelligentactuator.com/images/rcp2_ra10c.jpg Right image: http://cdn.shopify.com/s/files/1/0251/9611/files/BOOM_small.jpg?15468
Slide 25 – Non-Actuator Devices: Elements Left Image: Hocoma
Slide 26 – Non-Actuator Devices: Upper/Lower Limbs 1st image: Hocoma 2nd image (handSOME): http://cabrr.cua.edu/res/images/research/Handsomepic6.jpg 3rd image (GBO): http://roar.me.columbia.edu/projects/gbo/figures/gbo.jpg

## Slide 73: Fuentes de imágenes
Slide 26 – Non-Actuator Devices: Upper/Lower Limbs 4th image (ZeroG): http://www.aretechllc.com/img/passive/zgp1-n.jpg
Slide 27 – Non-Actuator vs. Robotic Devices Images: Created for slide pool
Slide 28-30 – Advantages and Limitations Icons: Created for slide pool
Slide 31 – Functional Electrical Stimulation Light bulb: http://theosophy.net/forum/topics/theosophists-and-the-light Muscle: http://cdn.inquisitr.com/wp-content/uploads/2011/06/build-leg-muscle.jpeg Electricity pattern: http://i.kinja-img.com/gawker-media/image/upload/s--v9hJqgOH--/c_fit,fl_progressive,q_80,w_636/187bzswqhpil0jpg.jpg FES: http://www.walkaide.com/en-US/news/PublishingImages/productimages/Bi-Flex-Production-4_tn.jpg
Slide 32 – FES: Elements Image: IISART Techindex
Slide 33 – FES: Stimulation Parameters Upper image: From Fuglevand et al. 1999, Force-frequency and fatigue properties of motor units in muscles that control digits of the human hand. Lower image: From Kesar et al. 2008, Effects of stimulation frequency versus pulse duration modulation on muscle fatigue.

## Slide 74: Fuentes de imágenes
Slide 34 – FES: Electrodes Images (surface & subcut.): Present. from Finetech Medical Ltd.: http://www.healthyaims.org/presentations06/Functional%20Electrical%20Stimulation% 20-%20Salisbury%20presentation%20March%203rd%2006.pdf
Slide 35-36 – Electrode Types Icons: Created for slide pool
Slide 38 – Advantages and Limitations Icons: Created for slide pool
Slide 40 – Sensor Technology Light bulb: http://theosophy.net/forum/topics/theosophists-and-the-light Sensor: Hocoma Display: http://clipartist.net/svg/monitor-screen-may-2011/ Sensor technology: Hocoma
Slide 41 – Sensor Technology: Elements Image: Hocoma
Slide 43 – Sensor Technology: Field of Application Icons: Created for slide pool

## Slide 75: Fuentes de imágenes
Slide 44 – Sensor Technology in Rehabilitation I Images: Presentation from Clemens
Slide 45 – Sensor Technology in Rehabilitation II Icons: Created for slide pool
Slide 46 – Sensor Technology: Advantages and Limitations Icons: Created for slide pool
Slide 48 – Virtual Reality Light bulb: http://theosophy.net/forum/topics/theosophists-and-the-light User input/tracking device: http://i-am-fast.com/Pictures/data-glove.jpg Display: http://clipartist.net/svg/monitor-screen-may-2011/ Virtual reality: IISART Techindex
Slide 50 – Virtual Reality: Principles Original slide: Prof. Dr.-Ing. Robert Riener, ETH Zurich
Slide 51 – Virtual Reality: Elements Image: IISART Techindex
Slide 52 – Virtual Reality: Hardware HMD: http://www.geeky-gadgets.com/wp-content/uploads/2012/10/Carl-Zeiss-OLED-Head-Mounted-Display.jpg BOOM: http://www.macs.hw.ac.uk/~hamish/9ig2/graphics/f3boomhf.GIF

## Slide 76: Fuentes de imágenes
Slide 52 – Virtual Reality: Hardware CAVE: http://www.jvrb.org/past-issues/3.2006/589/figure03.jpg Data glove: http://i-am-fast.com/Pictures/data-glove.jpg Control devices: http://cdn2.sbnation.com/assets/3757533/hydra-theverge-1_560.jpg
Slide 53 – Virtual Reality: Software (Architecture) Icons: Created for slide pool
Slide 54 – Virtual Reality: Field of Application Icons: Created for slide pool
Slide 55 – Virtual Reality: Devices Icons: Created for slide pool
Slide 56 – Virtual Reality: Immersive Devices Image: Created for slide pool
Slide 57 – Virtual Reality: Non-Immersive Devices Image: Created for slide pool
Slide 58-59 – Advantages and Limitations Icons: Created for slide pool

## Slide 77: Fuentes de imágenes
Slide 60 – Linkage to Neural Principles and Learning Motivation: Created for slide pool Feedback: http://lermagazine.com/wp-content/uploads/2014/01/1ITM-diabetes-iStock_13540.jpg Repetitions: Hocoma
Slide 62 – Brain Stimulation Light bulb: http://theosophy.net/forum/topics/theosophists-and-the-light Brain: Created for slide pool by Gokcen Akcali Electricity: http://i.kinja-img.com/gawker-media/image/upload/s--v9hJqgOH--/c_fit,fl_progressive,q_80,w_636/187bzswqhpil0jpg.jpg Brain stimulation: http://brainmodulation.com/wp-content/uploads/2014/06/brain-mod-assfn.jpg
Slide 63 – Brain Stimulation: Elements Magnetic coil: http://www.magstim.com/img/imagecache/8/e/1/d/cache_8e1deb172df266220a30b367e3b279d3.png Stimulator: http://www.rogue-resolutions.com/wp-content/uploads/2012/07/Rogue-Resolutions-DC-STIMULATOR-PLUS.jpg Electrodes: http://www.wired.com/wp-content/uploads/2014/05/brainstim-figure.jpg
Slide 64 – Brain Stimulation: Methods TMS: http://www.brainclinics.com/dynamic/media/1/images/rTMS_Figure1.png tDCS: http://www.drmueller-healthpsychology.com/i//tDCS_Device.jpg DBS: http://www.extremetech.com/wp-content/uploads/2013/07/Deep-brain-stimulation-640x353.jpg
Slide 65 – Brain Stimulation: TMS Image: http://2012books.lardbucket.org/books/beginning-psychology/section_17/5031a470f57cb20752c42fb4956e7c3f.jpg

## Slide 78: Fuentes de imágenes
Slide 66 – Brain Stimulation: tDCS image: http://davidileitman.com/wp-content/uploads/2014/04/tdcs.jpg
Slide 67 – TMS vs. tDCS TMS: http://www.brainclinics.com/dynamic/media/1/images/rTMS_Figure1.png tDCS: http://www.drmueller-healthpsychology.com/i//tDCS_Device.jpg