## Slide 1
Evidencia científica de las tecnologías avanzadas en rehabilitación.

## Slide 2: Evidencia científica de las tecnologías avanzadas en rehabilitación.
El contenido de esta presentación se basa en la presentación de IISART, revisada, traducida y adaptada por Centro Europeo de Neurociencias.
Puedes utilizar el contenido de esta presentación con tus pacientes y tus compañeros de trabajo, eso si, referencia siempre y en todo momento el origen y los autores de la misma.
Si el contenido de esta presentación va a ser utilizada en cualquier formación, curso, congreso, jornada, etc., se deberá pedir primero permiso a los autores de la misma.

## Slide 3: Audiencia
Clínicos
Investigadores
Ingenieros
Otros
Objetivo de aprendizaje:
Conocer la evidencia científica actual en relación a las nuevas tecnologías en rehabilitación.

## Slide 4: Razones para el uso de nuevas tecnologías
Sociedad
Tecnológico
Clínico
Envejecimiento de la población.
Coste sanitario
Carga en la vida diaria
Tecnología disponible
Rápido crecimiento
Uso en el hogar
Potencial de recuperación sin usar
Conocimiento basado en la evidencia
Notes: There are various reasons why new technologies are becoming more and more applied in rehabilitation. One group of such reasons can be summarized as societal drivers. These include for example the overaging of the population (in 2030 around 25% of people will be over 65; in 2050 this number will have more than doubled), the rising cost of health care and the increasing burden impairments have on daily life.
There is a therefore need for new approaches that can cope with the future demand. New technologies are very likely part of the solution to enable more efficient rehabilitation (higher intensity) which can also take place outside of hospitals. They might also help to lower health care costs and increase the part of recovery which the patients can do by themselves.
Another driving force is the current advanced state of available technology as well as the fast developement of new technologies. This opens up new fields of application and changes the attitude towards the use of new technologies. Nowadays for example technology gets more and more accepted in hospitals and rehabilitation centers. Progress in technology also makes it possible to bring therapy from the hospital into patients’ homes.
A third point that drives the application of new technologies in rehabilitation comes from the clinical side. Current recovery progress for conventional therapy still seems to have room for improvement. In addition, new evidence-based knowledge is continuously gained and pushed new treatment methods.
Historically Rehabilitation has been the poor relation in medicine
Absence of scientific rationale
Absence of evidence
No conventional rehabilitation procedures are any better than any other but intensity is important (Pomeroy)
Recovery of lower limb function (walking) is better than upper limb function (Hiraoka 2001)
Of a sample of patients with no active upper limb movement on admission:
14% experienced complete recovery
30% partial recovery
56 % had no recovery (Hendricks 2002)
5% of survivors with severe paresis regain upper limb function (Barecca 2001)
Can we do better?
For successful clinical use systems must be:
Robust and reliable
Motivating, engaging and easy for patients to use
Made possible by advances in electronic and software design, signal processing and control engineering
Demonstrate clinical benefit and cost-effectiveness
Driven by a better understanding of the neuroscience of motor learning and control

## Slide 5: Utilización de las nuevas tecnologías
Aprendizaje motor
Daño cerebral
Terapia
Valoraciones
Actividades diarias
Nuevas tecnologías para mejorar la eficacia y efectividad de la terapia.
...y valorar el progreso en la recuperación

## Slide 6: Potencial influencia de las nuevas tecnologías
Tecnología avanzada en rehabilitación
Repeticiones variadas y orientadas a un objetivo & feedback de ejecución exitosa.
Reduce el apoyo
Incremento del desafío
Input de movimiento y sensitivo
Fuerza muscular
Neuroplasticidad y aprendizaje motor
Mejora de la ejecución
Notes: From a presentation by Jane Burridge:
For normal motor learning to occur, the individual must be able to perform the task – even though performance may be imperfect. With repetition, feedback of performance, motivation, encouragement etc. performance improves. Where motor control is severely limited the individual is unable to perform the task and so cannot practice effectively and often receives negative or absent feedback, they may become discouraged and de-motivated. For an individual who has one normally functioning arm and hand the temptation is strong to perform tasks one handed – with the consequent learnt disuse effect.
By augmenting the individual’s performance using new technologies some of these problems can be overcome

## Slide 7: Contenidos
Terapia asistida por robots
Sistemas no motorizados
Estimulación eléctrica funcional (FES)
Tecnología de sensores
Realidad virtual
Estimulación cerebral

## Slide 8: Terapia asistida por robots
1

## Slide 9: Terapia asistida por robots: Extremidad inferior
Mejoras en la marcha
Efecto positive en la velocidad de la marcha, distancia caminada e implicación en actividades de la vida diaria.
Tiempo de rehabilitación
Los pacientes que no deambulan y están en una fase temprana de la rehabilitación son los que más se benefician de la terapia robótica.
Dependencia
Se podría evitar la dependencia en 1 de cada 5 personas si se utiliza Entrenamiento asistido por robots.
Effectividad
La terapia robótica en combinación con la “convencional” es más efectiva que la “convencional” sola.
(Mehrholz et al. 2017)
Notes: Mehrholz et al. 2013
Robotic gait therapy in combination with conventional therapy is more effective than physiotherapy alone.
Every fifth dependency in walking after stroke could be avoided if electromechanical assisted devices were used.
In particular non-ambulatory stroke patients in early rehabilitation profit from robot assisted therapy.
Electromechanical-assisted gait training in combination with physiotherapy increased the odds of participants becoming independent in walking but did not significantly increase walking or walking capacity.
People who receive electromechanical-assisted gait training in combination with physiotherapy after stroke are more likely to achieve independent walking than people who receive gait training without these devices. Specifically, people in the first three months after stroke and those who are not able to walk seem to benefit most from this type of intervention.
The use of electromechanical devices for gait rehabilitation of non-ambulatory people after stroke did not increase the risk of participants dropping out or dying during the intervention period
ability to walk at study end was not dependent on the type of device used in the studies The use of end-effector devices for gait rehabilitation significantly increased the walking velocity. The use of exsoskeleton devices for gait rehabilitation significantly decreased the walking velocity. in the absence of a direct empirical comparison between electromechanical-assisted gait training devices, this point warrants further investigation.
use of electromechanical-assisted devices in combination with physiotherapy in rehabilitation settings may improve walking function after stroke. Furthermore, adverse events, drop-outs and deaths do not appear to be more frequent in participants who received electromechanical or robotic-assisted gait training.
Problems: Heterogenious study variables (e.g. duration of therapy, severity of stroke and time after incident)
that every fifth dependency in walking ability after stroke could be avoidable if electromechanical-assisted devices are used. However, what remains unclear is the optimum amount of electromechanical-assisted gait training (optimal frequency, optimal duration in the use of assistive technologies and timing of application).
It appears that people in the acute and subacute phases after stroke profit more than people treated more than three months poststroke from this type of therapy (Analysis 3.1).
This systematic review provides evidence that the use of electromechanical- assisted gait training devices in combination with physiotherapy increases the chance of regaining independent walking ability for people after stroke. These results could be interpreted as preventing one participant from remaining dependent in walking after stroke for every five (95% CI 4 to 6) treated. However, this apparent benefit for patients is not supported by our secondary outcomes. Gait training devices were not associated with improvements in walking velocity nor walking capacity. It appears that the greatest benefits with regard to independence in walking and walking speed can be achieved in participants who are non-ambulatory at the start of the study and in those for whom the intervention is applied early post-stroke.
Significant homogeneous positive SESs for maximum gait speed, walking distance, peak heart rate, and basic ADL
Nonsignificant SESs were found for neurological functions, motor function of the paretic leg (synergy), muscle strength, comfortable gait speed and cadence.
Comfortable gait speed analysis showed that only patients in the early rehabilitation phase who were dependent in walking benefited from electromechanical-assisted gait training.
Veerbeek et al. 2014
Lower Limbs
16 RCTs
Pooling resulted in significant homogeneous positive SESs for maximum gait speed, walking distance, peak heart rate, and basic ADL. Nonsignificant SESs were found for neurological functions, motor function of the paretic leg (synergy), muscle strength, comfortable gait speed, cadence, step length, heart rate at rest, balance, walking ability, extended ADL, and quality of life. Subgroup analyses showed significant differences between poststroke phases. The analysis for comfortable gait speed showed that only patients in the early rehabilitation phase who were dependent in walking benefited from electromechanical-assisted gait training.
As regards balance, a significant homogeneous positive SES was found for the early rehabilitation phase (n= 4), a significant negative effect size for the late rehabilitation phase (n= 1), and anonsignificant SES for the chronic phase (n= 4). As regards walking ability, a significant homogeneous positive SES was found for patients in the early rehabilitation phase (n= 12), a significant negative effect size for the late rehabilitation phase (n= 1), and a nonsignificant homogeneous negative SES for the chronic phase (n =3

## Slide 11: Terapia asistida por robots: Extremidad superior
Mejoras a nivel proximal
Efecto significativo en la función motora del hombre y codo, fuerza muscular y reducción del dolor.
Mejoras distales
El Entrenamiento del codo y la muñeca mejora la función motora y la fuerza muscular.
Transferencia a actividades vida diaria
Mejora genérica de las actividades de la vida diaria y la función del brazo.
(Veerbeek et al. 2014)
Riesgos
No se incrementa el riesgo de lesion con un tratamiento intensive.
Tiempo recuperación
La terapia robótica mejora la función motora en un period de tiempo menor que la terapia convencional.
(Mehrholz et al. 2018)
(Veerbeek et al. 2014)
(Mehrholz et al. 2018)
(Sale et al. 2014)
Notes: Robot-assisted arm training improves generic activities of daily living as well as arm function, but not arm muscle strength.
The risk of patients when training with robot-assisted devices to drop out of therapy did not increase and adverse events were rare.
There is no evidence of harm when robot-assisted rehabilitation devices were used for training.
Training of the shoulder and elbow had a significant effect on motor function of the proximal part of the paretic arm (synergy), muscle strength, and pain.
Bilateral elbow and wrist practice showed significant effects for motor function of the paretic arm (synergy) and muscle strength.
Training of the shoulder in combination with elbow, wrist and hand resulted in nonsignificant effects on motor function of the paretic arm (synergy) and muscle strength of the distal part of the arm.
(Mehrholz et al. 2012)
The use of electromechanical-assistive devices in rehabilitation settings may improve generic activities of daily living. We also found evidence that arm function, but not arm muscle strength may improve. Furthermore, adverse events and drop outs do not appear to be more frequent in those participants who received electromechanical and robot-assisted arm training.
Problems: as Kwakkel 2008 pointed out, it is important to consider that robotic therapy uses robots simply as vehicles to apply many repetitions of arm training. It seems unlikely that therapy provided by robots will lead to better results than therapy provided by humans under the premise that intensity, amount and frequency of therapy are exactly comparable. One could argue that robot-assisted arm therapy after stroke is more effective in improving activities of daily living and arm function than other interventions only if the same number of practice repetitions is offered.
However, most of the included studies had an active control group which mostly matched the number of repetitions, but the number of repetitions was not exactly reported. This seems to be an important issue which has to be taken into account when discussing the effectiveness for the primary outcome.
potential advantage of electromechanical devices, as compared with conventional therapies,may be an increase in repetitions during arm training due to an increase of motivation to train. Additionally, because patients with electromechanical and robot-assistance are able to practice without a therapist, this type of training has the potential to increase the number of repetitions of practise.
Jane Burridge
The number of papers published concerning robots in therapy has increased rapidly. During a literature search (see Appendix C) fifty seven upper limb stroke specific papers from 1966-2005 were found. These can be categorized into clinical trials (of which there are two reviews (Prange et al., 2006; Teasell et al., 2005)), discussion and design papers.
EBRSR (Teasell et al) considered twelve randomised controlled trials (RCTs) whilst in their Systematic Review (Prange et al, 2006) considered eight studies (See Appendix D)
The reviews concluded:
“There is strong (Level 1a) evidence that senosorimotor training with robotic devices improves upper extremity functional outcomes, and motor outcomes of the shoulder and elbow. There is strong (Level 1a) evidence that robotic devices do not improve motor outcomes of the wrist and hand” (Teasell et al. 2006).
“Robot aided therapy of the proximal upper limb improves short- and long-term motor control of the paretic shoulder and elbow in subacute and chronic patients; however, we found no consistent influence on functional abilities. In addition, robot-aided therapy appears to improve motor control more than conventional therapy” (Prange 2006).
In looking at the twenty two clinical trials there was a wide variety in the variables which makes drawing conclusions from the trials difficult: subject numbers varied from one to fifty six; total robot exposure varied from four to thirty six hours; and eighteen different outcome measures were used (thirteen clinical and five robot).
The common themes that can be drawn however, are that firstly, the proportion of papers published using robots in upper limb post stroke therapy is small in comparison to therapy in general. Secondly, robots are regarded as having a role in assessment and treatment of patients (however, medium scale trials of one hundred and sixty patients have only just begun in the USA using InMotion 2 robots). Thirdly, the two clinical trial reviews agreed that robot aided therapy improves motor control of the proximal upper limb but disagreed concerning functional improvements.
It is not clear whether robot aided therapy really improves function at present. Future work needs to clarify the relationship between impairment and function, and the classification of outcome measures, as these both have important implications for the role of robots.
Prange et al. 2006
“Robot aided therapy of the proximal upper limb improves short- and long-term motor control of the paretic shoulder and elbow in subacute and chronic patients; however, we found no consistent influence on functional abilities. In addition, robot-aided therapy appears to improve motor control more than conventional therapy.” Results were statistically significant but not clinically. Moderate stroke patients might benefit more than severely affected patient.
Problems: only 1 study with subacute patients and 7 with chronic. Outcome measurements included wrist and hand improvements although only one study trained them (else outcome score might have been better). For functional improvement training of hand and wrist might be necessary to see an effect. Control modes of robots mixed passive, active-assisted and active-resisted but some might be much more beneficial. Compensation of gravity might lead to improvement in motor function (smaller effect of training).
Sale et al. 2014
53 subacute stroke patients, additional 30 sessions (45 minutes per session) of robot-assisted therapy or conventional therapy (6 weeks, 5 days per week) to standard inpatient therapy. Outcome measurements were FM, MAS-S and MAS-E. Secondary measures were pRom and MI. Statistically significant improvements for robot therapy in MAS-S and MAS-E but only a trend for conventional therapy. FM improved significantly in both groups. Robot-assisted therapy improved pRom and MI significantly while conventional therapy only improved MI significantly.
“Our results show that intensive robot-assisted treatment in subacute stroke patients may significantly reduce motor impairment in the paretic upper limb, with a statistically significant change in both pROM and MAS after 15 sessions of robotic treatment. At the end of the treatment (i.e., 30 sessions), FM and MI improved significantly in both groups, even if the improvement in FM was higher in the EG than in the CG after 15 sessions, confirming that intensive training provided by robotic device contributes to obtain better results than usual treatment at the early stage of rehabilitation.”
After 15 sessions of intensive robot-assisted rehabilitation therapy, moderate-to-severe upper limb impaired stroke survivors improved more than those who received intensive traditional therapy. This finding was also confirmed after 30 sessions, although FM and MI significantly improved in both groups at the end of the treatment, showing an advantage in robot-assisted therapy only in the early stage of rehabilitation training. Robot-assisted treatment provided in the subacute phase is able to effectively improve motor performance of the upper limb in a shorter time compared to usual intensive physiotherapy, thus accelerating the trend of motor recovery
Veerbeek et al. 2014
22 RCTs
Shoulder-elbow robotics
15 RCTs. Pooling resulted in significant homogeneous positive SESs for motor function of the proximal part of the paretic arm (synergy), muscle strength, and pain. Nonsignificant SESs were found for motor function of the paretic arm, motor function of the distal part of the paretic arm, muscle tone, arm-hand activities, basic ADL, and quality of life. Subgroup analyses revealed no significant differences between poststroke phases.
Elbow-wrist robots (bilateral mode)
2 RCTs. Meta-analyses showed significant homogeneous positive SESs for motor function of the paretic arm (synergy) and muscle strength. Subgroup analyses revealed no significant differences between phases poststroke.
Shoulder-elbow-wrist-hand robotics
2 RCTs. Pooling the data resulted in nonsignificant SESs for both motor function of the paretic arm (synergy) and muscle strength of the distal part of the arm. Subgroup analyses revealed no significant differences between poststroke phases.
There is strong evidence for PT interventions favoring intensive high repetitive task-oriented and task-specific training in all phases poststroke. Effects are mostly restricted to the actually trained functions and activities.
Upper Limbs
Shoulder-elbow robotics
Pooling resulted in significant homogeneous positive SESs for motor function of the proximal part of the paretic arm (synergy), muscle strength, and pain. Nonsignificant SESs were found for motor function of the paretic arm, motor function of the distal part of the paretic arm, muscle tone, arm-hand activities, basic ADL, and quality of life. Subgroup analyses revealed no significant differences between poststroke phases
Meta-analyses showed significant homogeneous positive SESs for motor function of the paretic arm (synergy) and muscle strength. Subgroup analyses revealed no significant differences between phases poststroke.
Pooling the data resulted in nonsignificant SESs for both motor function of the paretic arm (synergy) and muscle strength of the distal part of the arm. Subgroup analyses revealed no significant differences between poststroke phases.
Sensorimotor training with robotic devices improves functional and motor outcomes of the shoulder and elbow; however, it does not improve functional and motor outcomes of the wrist and hand (Teasell et al. 2006).
“There is strong (Level 1a) evidence that senosorimotor training with robotic devices improves upper extremity functional outcomes, and motor outcomes of the shoulder and elbow. There is strong (Level 1a) evidence that robotic devices do not improve motor outcomes of the wrist and hand” (Teasell et al. 2006).
Kwakkel et al. (2008) “Effects of Robot-assisted therapy on upper limb recovery after stroke: A Systematic Review,” Neurorehabilitation and Neural Repair 22(2):111-121.
Strong evidence for improved motor control (impairment) and some evidence for improved function [Kwakkel 2008, EBRSR & Prange 2006]
Proximal training = proximal benefit
Possibly people with moderate impairment respond better
Better understanding of how therapy should be applied – dose, activities, bilateral, resisted / assisted
Include hand and wrist / order of training
Potential for combining functional training with robot training
Significant reduction in motor impairment of the paretic upper limb in subacute stroke patients. Motor function improved in a shorter time compared to usual physiotherapy (Sale et al. 2014).

## Slide 13: Coste efectividad
Chart: 
| years to break even
Robot-assisted therapy | 2.08
Conventional therapy | 1.6
  Los costes de la terapia convencional de Entrenamiento de la marcha son bajos.
  Los costes fijos de la terapia asistida por robot (compra del Sistema) son altos.
  En el largo plazo, la terapia asistida por robot es major en cuanto a coste efectividad.
Chart: 
| 1st year | 2nd year | 3rd year | 4th year | 5th year
Robot-assisted therapy | -157000 | -8750 | 139500 | 287500 | 436000
Conventional therapy | -45000 | 30500 | 106000 | 181000 | 256000
Profit
Loss
Cost [€]
Time from start of treatment [Years]
Type of gait training
Years to break even
  (Morrison 2011, Wagner et al. 2011)
Notes: Robotic gait therapy economically outperformed non-robotic therapy when analyzed over a five years time frame.S. Morrison, Financial Feasibility of Robotics in Neurorehabilitation. Top Spinal Cord Inj Rehabil 2011;17(1):77–81
Wagner et al. (2011) An economic analysis of robot-assisted therapy for long-term upper-limb impairment after stroke. Stroke 42: 2630-2632.
A total of 127 participants were randomized to usual care plus robot therapy (n49), usual care plus intensive comparison therapy (n50), or usual care alone (n28). The average cost of delivering robot therapy and intensive comparison therapy was $5152 and $7382, respectively (P0.001), and both were significantly more expensive than usual care alone (no additional intervention costs). At 36 weeks postrandomization, the total costs were comparable for the 3 groups ($17 831 for robot therapy, $19 746 for intensive comparison therapy, and $19 098 for usual care). Changes in quality of life were modest and not statistically different.
The added cost of delivering robot or intensive comparison therapy was recuperated by lower healthcare use costs compared with those in the usual care group. However, uncertainty remains about the cost-effectiveness of robotic-assisted rehabilitation compared with traditional rehabilitation.
NeReBot
Robotic-assisted arm therapy has in the long term lower costs than conventional therapy when moderate-to-low cost devices are used efficiently (several robots per therapist)

## Slide 15: Coste efectividad II
  En un entrenamiento asistido por robot de 5 semanas con un dispositivo que tiene un coste medio-moderado, el periodo de recuperación y alta del hospital puede ser de 1.2 días menor. Cualquier reducción igual o superior resultaría en un ahorro de dinero (Stefano et al. 2014).
“La tecnología robótica puede ser una ayuda valiosa y económicamente sostenible en
el manejo de la rehabilitación del paciente post ictus.”, Stefano et al. 2014
Chart: Cost (€)
5 weeks of robotic rehabilitation | 328.04
1 day of hospitalization | 273.64
Chart: 
| Time
1 day of hospitalization | 1
5 weeks robotic therapy | 25
273.64 €
328.04 €
Notes: Calculation with low therapist income (33’040 per year) compared to Morrison et al. 2011 (~60’530)
Costs of robotic interventions can be considered easily affordable, if delivered through easy-to-use and moderate-to-low cost devices. Depending on the therapy protocol costs may even be eliminated. Study focused on acute stroke patients.
Robot-assisted group therapy (RAGT) in combination with individual arm therapy (IAT) was equally effective as a double session of IAT regarding the restoration of upper limb motor functions in moderate to severely affected subacute patients with stroke. The treatment costs for RAGT were less.
Hesse et al. 2014

## Slide 16: Dispositivos no motorizados
2

## Slide 17: Evidencia clínica de los dispositivos no motorizados
Efectividad
Iguala las ganancias de la terapia convencional
Funcionalidad
El soporte de peso del brazo mejora los movimientos de la mano, importante para la mejora de la habilidad funcional
Rango de movimiento
Incrementa el rango de movimiento del brazo y la mano
Control de sinergias
Ayuda a reducer el acoplamiento anormal entre el hombre y codo.
(Prange et al. 2014)
(Kloosterman et al. 2010, Krabben et al. 2012)
(Bartolo et al. 2014)
(Krabben et al. 2012)
Notes: Conversely, arm weight support rehabilitation based on the use of passive orthotic devices has been shown to improve features of hand movements that may be considered crucially important for achieving a positive recovery of upper limb motor control (Morasso, 1981; Wisneski and Johnson, 2007) and may be related to enhanced functional ability.
The Armeo, developed by the makers of the Lokomat ( www.hocoma.ch ), is a counterbalanced arm support with an instrumented gripper that allows functional movement against resistance in a virtual reality environment [ 77, 78 ] . A recently published RCT involving chronic stroke survivors compared semiautonomous ET on T-WREX, a gravity-support device similar to the Armeo, with semiautonomous conventional ET in which a tabletop was used to provide gravity support [ 79 ] . The size of the improved benefit with T-WREX was small, and the self-reported functional use of the upper extremity was not different between groups. The benefits of the T-WREX were therefore characterized as modest and functionally insignificant.
A much simpler gravity support system, the Armeo Boom, was recently commercially released. A study with a precursor of this device, the “freebal,” in ten patients with mild hemiparesis found that gravity compensation facilitated active arm movement excursions without impairing motor control. It was concluded that gravity compensation may be a valuable modality in conventional or robot-aided therapy to increase the intensity of training for mildly impaired patients; [ 80 ] however this remains to be proven in clinical trials.
Arm support training –
  facilitates activation of agonists
  possibly reduces abnormal coupling
Prange et al. 2009
Muscle activation patterns during movements, with and without gravity compensation, showed that the pattern of muscle activity, as represented by the change of average SRE values across specific aspects of movement, was not influenced by gravity compensation.
level of muscle activity was 25% to 50% lower with gravity compensation in all muscles
movement time, movement symmetry, and joint angle excursions were comparable in both conditions
Kloosterman et al. 2010
gravity compensation increases range of motion of the upper limb [12,14] because of the positive effect on pathological muscle synergies between shoulder abduction and elbow flexion [14].
Krabben et al. 2012
After 6 weeks of moderately intense gravity compensated reach training, a sample of 7 chronic stroke patients showed improved arm function, as indicated by a median increase of 3 points on the FM scale. Subjects also significantly increased the active work area of the hand as indicated by the normalized circle area, whereas circle roundness remained almost constant. Statistically significant
changes were observed in excursions of EP and EA, accompanied by increasing trends in excursions of AR and EF. The occurrence of synergistic movement patterns was similar before and after training.
Application of gravity compensation has been shown to reduce the influence of abnormal coupling between the shoulder and elbow [15,29] which is likely to result in rounder circles.
Bartolo et al. 2014
significant improvement in hand range of motion was achieved by the patients in the SG. These results indicate a functional improvement obtained with arm weight support therapy, and therefore
the possibility of achieving a wider set of movements directly related to a wider work-space dimension.
arm weight support rehabilitation leads to reduced NJ and to increased hand RoM, which is crucially important for positive recovery of upper limb motor control (Morasso, 1981; Wisneski
and Johnson, 2007), and possibly related to improved functional ability in executing ADL.
Prange et al. 2014
Improvements in arm function and activity of subacute stroke participants after AS training combined with computerized exercises matched the gains after CON sessions of equal dosage.

## Slide 18
For Professionals - Tyromotion
Home page - Hocoma Knowledge Platform

## Slide 19: Estimulación eléctrica funcional (FES)
3

## Slide 20: Evidencia clínica de FES
Muñeca y mano
Efecto positivo en la fuerza muscular y la función motora
Funcionalidad
Mejora la función de la extremidad superior y el procesamiento motor.
Dolor
Reducción significativa del dolor
(Arantes et al. 2007)
Espasticidad
Reduce la espasticidad
Velocidad de la marcha
FES con electrodos de superficie e implantados incrementan la velocidad de la marcha
(Wilson et al. 2014)
(Ring and Weingarden 2007)
(Daly and Ruff 2007, Hara 2008)
(Kottink 2007, Veerbeek et al. 2014)
Notes: Evidence for improved function and reduced impairment [EBRSR 2006] - improvement may be greater in acute stroke [Wang 2002]
Improvement is enhanced when stimulation is voluntary activated[de Kroon 2005]
Veerbeek et al. 2014
For dropped foot of central neurological origin:
Meta-analysis of three studies on skin surface-applied FES found that it increased gait speed by a mean difference of 0.18 metres /second (95% CI 0.08 to 0.28) in stroke patients (n = 36) compared with conventional therapy (n = 35) [Robbins et al 2006]
A case series of 140 patients undergoing skin surface FES, stroke patients (n = 111) showed an increase in walking speed of 12% (0.07metres/second) and a decrease in effort of 18% (-0.16 beats/metre) (measured by a physiological cost index) when using the stimulator (orthotic effect) compared with baseline. At 4.5-month follow-up there was a 14% (0.08 metres/second) increase in walking speed and a 19% (-0.17 metres/second) reduction in effort. [Taylor 1999]
For RCTs using implanted electrodes
FES was compared with conventional therapy in 29 patients. FES resulted in a 23% improvement in walking speed measured with the six-minute walking test (6MWT), compared with an improvement in the control group of 3% (p = 0.010) [Kottink 2007]
Response to coordination exercise, overground gait training, and weight-supported treadmill training, was compared with and without functional neuromuscular stimulation (FNS) using intramuscular (IM) electrodes (FNS-IM) for 32 chronic stroke patients. No significant differences in the 6MWT were found between the group with implanted electrodes (post-treatment mean/median walking distance 252.2 metres) and the control group who received physiotherapy training (post-treatment mean/median walking distance 165.9 metres; p = 0.184) [Daly 2006].
For upper limb:
A review of 19 clinical trials evaluating the effect of ES on the recovery of upper limb motor control following stroke found that positive results were more common when electrical stimulation was triggered by voluntary movement rather than when non-triggered electrical stimulation was used. There was no relation between the effect of ES and other characteristics examined. [de Kroon 2005]
a single-site, pilot, RCT of adults with chronic shoulder pain after stroke. Participants were randomized to receive a 3-wk treatment of single-lead PNS or usual care. Twenty-five participants were recruited, 13 to PNS and 12 to usual care. There was a significantly greater reduction in pain for the PNS group compared with the controls, with significant differences at 6 and 12 wks after treatment. [Wilson 2014]
Wrist and finger muscles
Positive effects of FES on muscle strength, tonus, motor function and limb use in daily routine (Arantes et al. 2007). Moderate evidence for improved dexterity and limited evidence on motor coordination and independency in self-care activities. There is no evidence of gains in active range of motion.
Problem:
Diversity of protocols, participants’ characteristics and instrumentation prevented pooling of results.
de Kroon et al10 reviewed the relationship between stimulation parameters and clinical outcome in studies using electrical stimulation (ES) to improve motor control of upper extremity in stroke.
Motor stimulation can be applied by neuromuscular electrical stimulation with pre-programmed system with no active client involvement, EMG triggered electrical stimulation or positional feedback stimulation training both of which involve voluntary muscle contraction to trigger the ES. In review of 19 studies that fit the criteria, there was no relationship detected between the stimulation parameters (frequency, amplitude, pulse duration), duration of stimulation, subject characteristics and clinical outcome. There was a suggestion that a triggered stimulation may be more effective than the non-triggered stimulation in improving motor control.9,10 Research does suggest that parameters are important to the muscle contraction. But muscle contraction is the desired outcome and parameters are adjusted to achieve this.10 Often FES units have preprogrammed protocols.4 There is some research looking at trying to find parameters that maximize contraction and minimize fatigue.12 The triggered stimulus introduces the aspect of the cognitive component.6,9,10 Animal research studies have shown behavioural experiences which are meaningful, and require a cognitive intent, tend to have task specific cortical reorganization with development of motor skills.10 In a study looking at repeated stimulation of peroneal nerve, Khaslavskaia and Sinkjaer13 concluded that “cortical excitability modulated by peripheral nerve stimulation is focally and task specifically affected by voluntary cortical drive.”
The importance of being actively engaged in initiating or producing the movement may be a significant component in promoting recovery. 5
Lower Extremity Applications
In the Evidence Based Review of Stroke Rehabilitation 10th edition ( EBRSR) review of FES in the lower extremity, they state that “There is strong level 1A evidence that FES and gait training results in improvements in hemiplegic gait”.12
Initial use of FES was for electrical stimulation of peroneal nerve to treat weakness of ankle dorsiflexion or foot drop.4,5,6 There are systems available that consist of an heel sensor, stimulator and electrodes.4,5 The electrodes are place over common peroneal nerve cathode near head of fibula and anode over tibialis anterior. The heel sensor detects the pressure and tilt of the leg to turn on tibialis anterior at toe off and turn off tibialis anterior at heel strike.4
Results of studies of lower limb electrical stimulation
- Improved walking ability6
- Increased isometric contractions of dorsiflexors and plantarflexors6
- Decreased cocontraction4
With EMG triggering
- Increased mobility
- Increased voluntary EMG activity6
With a neuroprosthesis system, adding stimulation of knee and hip muscles
- Improved gait performance
- Motor learning progressed to gait training without neuroprosthesis6
Use of FES combined with physiotherapy or biofeedback produces superior results in
ambulation scores than any individual treatment alone.5
Burridge et al found increased walking speed with stimulation of peroneal nerve.14
This is not a common treatment for foot drop in North America. Some of the issues are accurate electrode placement, medial and lateral ankle control, requires custom AFO.6
There is evidence of motor relearning with peroneal nerve stimulation. The problems are accurate surface electrode placement, costs of invasive procedures for the implanted systems, complications of dealing with medial and lateral control as well as dorsiflexion. There is a distinct lack of large randomized control studies to look at the effectiveness of peroneal nerve stimulation for dorsiflexion.6
Functional Electrical Therapy (FET) is patterned multi-channel electrical stimulation acting as a neural prosthesis activating several muscles during gait. It assists with walking when there is little or no muscle activity in the leg. This can prevent disuse atrophy, discourage compensatory gait patterns, maintain some sensory motor input. Preliminary findings for a recent trial with hemiplegic patients, Popovic,5 show notably better recovery of walking with FET than with only conventional therapy. Popovic5 proposes that in the acute stage, the combined effect of therapy generated and spontaneous recovery can accelerate functional recovery. FET may be facilitating cortical reorganization in the acute stages of recovery.5
Results
Changes in corticospinal excitability can be achieved with repetitive stimulation of the common peroneal nerve 4. This may be a result of activating the motor and sensory fibers and changes in muscle fibre properties.4
Benefits are increase strength, decrease spasticity,14 increased muscle extensibility4 Cortical reorganization, cortical connectivity may be modified with high frequency sensory stimulation.4
Stimulation of ankle PF Improves ground clearance, decreased extensor tone and decreased swing time.4
UE research results
EBRSR review of FES in treatment of the upper extremity,” There is strong (Level 1A) evidence that FES treatment improves upper extremity function in acute stroke”. 12 “There is conflicting (level 4) it evidence that functional electrical stimulation reduces pain improves function and reduces subluxation following stoke.”12 There are limited randomized studies, with methodology variability but the results do indicate that there is some positive effect on upper extremity motor learning. With more significant results in the acute stage and those with milder impairment. These were studies looking at wrist
extension.6 In studies with biofeedback or EMG triggering NMES, there were gains made in motor recovery with some improvement in activity. 6
A Cochrane review of electrical stimulation for preventing and treating post stroke shoulder pain found 4 randomized control studies (170 subjects). There was no significant change in pain intensity or incidence, there was a significant effect in improving passive pain-free range of lateral rotation of the humerus with a decrease in subluxation. There was no significant effect on motor recovery. 15
There has been a trial done with a percutaneous system with a reduction in pain in chronic stroke survivors.6 Some of the technology used for upper extremity stimulation systems for the spinal cord population, neuroprostheses, have had limited application to stroke population. The movement is limited to a few functional activities namely opening and closing the hand. If tone is an issue, the increased effort to do the task often increases the tone, affecting the quality and outcome of the intended movement. In some trials with a neuroprosthesis there have been significant improvements reported. 6 According to Sheffler6 there is no clinically viable hand neuroprosthesis system currently available to meet the needs of the hemiplegic arm and hand, more research is needed. A feasible system would require the ability to facilitate bilateral tasks, permit distal and proximal control, be a compact size to ensure ambulation is not encumbered, stimulate weak and inhibit overactive muscle and not compromise intact arm.6
Results
- Improved hand and upper limb function in ADLs 3
- Decreased spasticity3,8,9
- Decreased shoulder pain3
Better outcomes with FES combined with functional task component practice8
1. Yan TB, Hui-Chan CWY, Li LSW. Functional electrical stimulation improves motor
recovery of the lower extremity and walking ability of subjects with first acute stroke – a
randomized placebo – controlled trial. Stroke 36(1): 80-85.
2. Peckman PH and Knutson JS. Functional electrical stimulation for neuromuscular
applications. Ann. Rev. Biomed. Eng. 2005. 7:327-60.
3. Ring H and Weingarden H. Neuromodulation by functional electrical stimulation (FES)
of limb paralysis after stroke. Acta Neurochir Suppl 2007; 97(1): 375-380.
4. Sujith OK. Functional electrical stimulation in neurological disorders. European journal
of Neurology 2008; 15: 437-444.
5. Popovic DB and Sinkjaer T. Neuromodulation of lower limb monoparesis: functional
electrical therapy of walking. Acta Neurochir Suppl 2007; 97(1): 387-393.
6. Sheffler LR and Chae J. Neuromuscular electrical stimulation in neurorehabilitation.
Muscle Nerve 2007; 35:562-590.
7. Bogey R and Hornby TG. Gait training strategies utililzed in poststroke Rehabilitation:
are we really making a difference? Top Stroke Rehabil 2007; 14(60): 1-8.
8. Daly, JJ and Ruff RL. Construction of efficacious gait and upper limb functional
interventions based on brain plasticity evidence and model-based measures for stroke
patients. The Scientific World journal 2007: 7: 2031-2045.
9. Hara Y. Neurorehabilitation with new functional electrical stimulation for hemiparetic
upper extremity in stroke patients. J Nippon Med Sch 2008: 75: 3-14.
10. de Kroon JR, Ijzerman MJ, Chae J, Lankhorst GJ, Zilvold G. Relation between
stimulation characteristics and clinical outcome in studies using electrical stimulation to
improve motor control of the upper extremity in stroke. J Rehabil Med 2005; 37: 65-74.
11. Electrotherapy: Evidence-Based Practice. Sheila Kitchen and Sarah Bazin. Churchill
Livingston 2002, New York.
12. Baldwin ERL, Klakowicz PM, Collins DF. Wide-pulse-width, high frequency
neuromuscular stimulation: implications for functional electrical stimulation. J Appl
Physiol 2006;101:228-240.
13. Khaslavskaia s and Sinkjaer T. Motor cortex excitability following repetitive electrical
stimulation of the common peroneal nerve depends on the voluntary drove. Exp Brain
Res 2005; 162:497-502.
14. Evidence Based Review of Stroke Rehabilitation 10th edition. www.ebrsr.com.
15. Price CL, Pandyan AD. Electrical stimulation for preventing and treating post-stroke
shoulder pain: a systematic Cochrane review. Clin Rehabil 2001: Feb 15(1) 5-19.
Limitations
•Lack of adequately powered, well designed trials
•Insufficient current evidence for UK NICE approval, but recommended for ‘consideration’ in the UK RCP Stroke Guidelines
• All studies show wide variation in response - can we be more effective in targeting potentially ‘good responders’
•Meta-analysis is difficult because of different methodologies
Although there have been positive results with use of FES, to generalize and present a protocol for FES as a treatment is difficult. The problem lies with variability in methodology, limited random control studies, lack of standardized treatment protocols, variability in population utilized ( acute vs chronic).1,14 There is a definite need for large, multicentre, randomized clinical trials with defined population4 and evaluation of immediate and long term outcomes.6 It is difficult to determine exact parameters for electrical stimulation due to many confounding variables.10 There is further research required to examine and determine optimal dose and parameters.4,6 Techniques and systems need to be improved to encourage compliance.6 Lack of studies comparing FES with EMG triggered FES and neuroprostheses.6 Research has shown: FES can be used for the hemiparetic population that demonstrates limited residual movement.6 There does appear to be some limited evidence to support use of FES for shoulder pain and to decrease subluxation. Better outcomes with task specific activities than with generalized function.3,10 When using FES, repetition, novelty, active contribution 5,6,13 and function are key points for achieving motor relearning.6
There is a definite lack of large scale research to definitively support or dismiss the use of FES in treatment of hemiplegic limbs in stroke. There appears to be a push toward increased use of technology with robot arms and neuroprostheses as treatment adjuncts. The cost of this technology may prevent immediate access for clients in our health care system. Regardless, the emphasis is still on tapping into motor learning and neuroplasticity using techniques of repetition and task specific training to improve functional outcomes. Research does provide some support for utilizing FES in promoting motor relearning and with further refined research there will likely be the development of more definitive protocols for treatment.
Literature
Robbins SM, Houghton PE, Woodbury MG et al. (2006) The therapeutic effect of functional and transcutaneous electric stimulation on improving gait speed in stroke patients: a meta-analysis. Archives of Physical Medicine & Rehabilitation 87: 853–859.
Taylor PN, Burridge JH, Dunkerley AL et al. (1999) Clinical use of the Odstock dropped foot stimulator: its effect on the speed and effort of walking. Archives of Physical Medicine & Rehabilitation 80: 1577–1583.
Daly JJ, Roenigk K, Holcomb J et al. (2006) A randomized controlled trial of functional neuromuscular stimulation in chronic stroke subjects. Stroke 37: 172–178.
Kottink AI, Hermens HJ, Nene AV et al. (2007) A randomized controlled trial of an implantable 2-channel peroneal nerve stimulator on walking speed and activity in poststroke hemiplegia. Archives of Physical Medicine & Rehabilitation 88: 971–978.

## Slide 22: Tecnología de sensores
4

## Slide 23: Evidencia clínica de tecnología de sensores
Miembro superior
Mejora de la función del brazo
Funcionalidad
Incremento del espacio de trabajo.
Compensaciones
Reducción de los movimientos compensatorios del tronco.
(Wittmann et al. 2016)
Motivación
Mejora de la adherencia a la terapia
(Wittmann et al. 2016)
(Wittmann et al. 2015)
(Wittmann et al. 2015)
(Wittmann et al. 2016)
(Wittmann et al. 2016)
Notes: Evidence for improved function and reduced impairment [EBRSR 2006] - improvement may be greater in acute stroke [Wang 2002]
Improvement is enhanced when stimulation is voluntary activated[de Kroon 2005]
Veerbeek et al. 2014
For dropped foot of central neurological origin:
Meta-analysis of three studies on skin surface-applied FES found that it increased gait speed by a mean difference of 0.18 metres /second (95% CI 0.08 to 0.28) in stroke patients (n = 36) compared with conventional therapy (n = 35) [Robbins et al 2006]
A case series of 140 patients undergoing skin surface FES, stroke patients (n = 111) showed an increase in walking speed of 12% (0.07metres/second) and a decrease in effort of 18% (-0.16 beats/metre) (measured by a physiological cost index) when using the stimulator (orthotic effect) compared with baseline. At 4.5-month follow-up there was a 14% (0.08 metres/second) increase in walking speed and a 19% (-0.17 metres/second) reduction in effort. [Taylor 1999]
For RCTs using implanted electrodes
FES was compared with conventional therapy in 29 patients. FES resulted in a 23% improvement in walking speed measured with the six-minute walking test (6MWT), compared with an improvement in the control group of 3% (p = 0.010) [Kottink 2007]
Response to coordination exercise, overground gait training, and weight-supported treadmill training, was compared with and without functional neuromuscular stimulation (FNS) using intramuscular (IM) electrodes (FNS-IM) for 32 chronic stroke patients. No significant differences in the 6MWT were found between the group with implanted electrodes (post-treatment mean/median walking distance 252.2 metres) and the control group who received physiotherapy training (post-treatment mean/median walking distance 165.9 metres; p = 0.184) [Daly 2006].
For upper limb:
A review of 19 clinical trials evaluating the effect of ES on the recovery of upper limb motor control following stroke found that positive results were more common when electrical stimulation was triggered by voluntary movement rather than when non-triggered electrical stimulation was used. There was no relation between the effect of ES and other characteristics examined. [de Kroon 2005]
a single-site, pilot, RCT of adults with chronic shoulder pain after stroke. Participants were randomized to receive a 3-wk treatment of single-lead PNS or usual care. Twenty-five participants were recruited, 13 to PNS and 12 to usual care. There was a significantly greater reduction in pain for the PNS group compared with the controls, with significant differences at 6 and 12 wks after treatment. [Wilson 2014]
Wrist and finger muscles
Positive effects of FES on muscle strength, tonus, motor function and limb use in daily routine (Arantes et al. 2007). Moderate evidence for improved dexterity and limited evidence on motor coordination and independency in self-care activities. There is no evidence of gains in active range of motion.
Problem:
Diversity of protocols, participants’ characteristics and instrumentation prevented pooling of results.
de Kroon et al10 reviewed the relationship between stimulation parameters and clinical outcome in studies using electrical stimulation (ES) to improve motor control of upper extremity in stroke.
Motor stimulation can be applied by neuromuscular electrical stimulation with pre-programmed system with no active client involvement, EMG triggered electrical stimulation or positional feedback stimulation training both of which involve voluntary muscle contraction to trigger the ES. In review of 19 studies that fit the criteria, there was no relationship detected between the stimulation parameters (frequency, amplitude, pulse duration), duration of stimulation, subject characteristics and clinical outcome. There was a suggestion that a triggered stimulation may be more effective than the non-triggered stimulation in improving motor control.9,10 Research does suggest that parameters are important to the muscle contraction. But muscle contraction is the desired outcome and parameters are adjusted to achieve this.10 Often FES units have preprogrammed protocols.4 There is some research looking at trying to find parameters that maximize contraction and minimize fatigue.12 The triggered stimulus introduces the aspect of the cognitive component.6,9,10 Animal research studies have shown behavioural experiences which are meaningful, and require a cognitive intent, tend to have task specific cortical reorganization with development of motor skills.10 In a study looking at repeated stimulation of peroneal nerve, Khaslavskaia and Sinkjaer13 concluded that “cortical excitability modulated by peripheral nerve stimulation is focally and task specifically affected by voluntary cortical drive.”
The importance of being actively engaged in initiating or producing the movement may be a significant component in promoting recovery. 5
Lower Extremity Applications
In the Evidence Based Review of Stroke Rehabilitation 10th edition ( EBRSR) review of FES in the lower extremity, they state that “There is strong level 1A evidence that FES and gait training results in improvements in hemiplegic gait”.12
Initial use of FES was for electrical stimulation of peroneal nerve to treat weakness of ankle dorsiflexion or foot drop.4,5,6 There are systems available that consist of an heel sensor, stimulator and electrodes.4,5 The electrodes are place over common peroneal nerve cathode near head of fibula and anode over tibialis anterior. The heel sensor detects the pressure and tilt of the leg to turn on tibialis anterior at toe off and turn off tibialis anterior at heel strike.4
Results of studies of lower limb electrical stimulation
- Improved walking ability6
- Increased isometric contractions of dorsiflexors and plantarflexors6
- Decreased cocontraction4
With EMG triggering
- Increased mobility
- Increased voluntary EMG activity6
With a neuroprosthesis system, adding stimulation of knee and hip muscles
- Improved gait performance
- Motor learning progressed to gait training without neuroprosthesis6
Use of FES combined with physiotherapy or biofeedback produces superior results in
ambulation scores than any individual treatment alone.5
Burridge et al found increased walking speed with stimulation of peroneal nerve.14
This is not a common treatment for foot drop in North America. Some of the issues are accurate electrode placement, medial and lateral ankle control, requires custom AFO.6
There is evidence of motor relearning with peroneal nerve stimulation. The problems are accurate surface electrode placement, costs of invasive procedures for the implanted systems, complications of dealing with medial and lateral control as well as dorsiflexion. There is a distinct lack of large randomized control studies to look at the effectiveness of peroneal nerve stimulation for dorsiflexion.6
Functional Electrical Therapy (FET) is patterned multi-channel electrical stimulation acting as a neural prosthesis activating several muscles during gait. It assists with walking when there is little or no muscle activity in the leg. This can prevent disuse atrophy, discourage compensatory gait patterns, maintain some sensory motor input. Preliminary findings for a recent trial with hemiplegic patients, Popovic,5 show notably better recovery of walking with FET than with only conventional therapy. Popovic5 proposes that in the acute stage, the combined effect of therapy generated and spontaneous recovery can accelerate functional recovery. FET may be facilitating cortical reorganization in the acute stages of recovery.5
Results
Changes in corticospinal excitability can be achieved with repetitive stimulation of the common peroneal nerve 4. This may be a result of activating the motor and sensory fibers and changes in muscle fibre properties.4
Benefits are increase strength, decrease spasticity,14 increased muscle extensibility4 Cortical reorganization, cortical connectivity may be modified with high frequency sensory stimulation.4
Stimulation of ankle PF Improves ground clearance, decreased extensor tone and decreased swing time.4
UE research results
EBRSR review of FES in treatment of the upper extremity,” There is strong (Level 1A) evidence that FES treatment improves upper extremity function in acute stroke”. 12 “There is conflicting (level 4) it evidence that functional electrical stimulation reduces pain improves function and reduces subluxation following stoke.”12 There are limited randomized studies, with methodology variability but the results do indicate that there is some positive effect on upper extremity motor learning. With more significant results in the acute stage and those with milder impairment. These were studies looking at wrist
extension.6 In studies with biofeedback or EMG triggering NMES, there were gains made in motor recovery with some improvement in activity. 6
A Cochrane review of electrical stimulation for preventing and treating post stroke shoulder pain found 4 randomized control studies (170 subjects). There was no significant change in pain intensity or incidence, there was a significant effect in improving passive pain-free range of lateral rotation of the humerus with a decrease in subluxation. There was no significant effect on motor recovery. 15
There has been a trial done with a percutaneous system with a reduction in pain in chronic stroke survivors.6 Some of the technology used for upper extremity stimulation systems for the spinal cord population, neuroprostheses, have had limited application to stroke population. The movement is limited to a few functional activities namely opening and closing the hand. If tone is an issue, the increased effort to do the task often increases the tone, affecting the quality and outcome of the intended movement. In some trials with a neuroprosthesis there have been significant improvements reported. 6 According to Sheffler6 there is no clinically viable hand neuroprosthesis system currently available to meet the needs of the hemiplegic arm and hand, more research is needed. A feasible system would require the ability to facilitate bilateral tasks, permit distal and proximal control, be a compact size to ensure ambulation is not encumbered, stimulate weak and inhibit overactive muscle and not compromise intact arm.6
Results
- Improved hand and upper limb function in ADLs 3
- Decreased spasticity3,8,9
- Decreased shoulder pain3
Better outcomes with FES combined with functional task component practice8
1. Yan TB, Hui-Chan CWY, Li LSW. Functional electrical stimulation improves motor
recovery of the lower extremity and walking ability of subjects with first acute stroke – a
randomized placebo – controlled trial. Stroke 36(1): 80-85.
2. Peckman PH and Knutson JS. Functional electrical stimulation for neuromuscular
applications. Ann. Rev. Biomed. Eng. 2005. 7:327-60.
3. Ring H and Weingarden H. Neuromodulation by functional electrical stimulation (FES)
of limb paralysis after stroke. Acta Neurochir Suppl 2007; 97(1): 375-380.
4. Sujith OK. Functional electrical stimulation in neurological disorders. European journal
of Neurology 2008; 15: 437-444.
5. Popovic DB and Sinkjaer T. Neuromodulation of lower limb monoparesis: functional
electrical therapy of walking. Acta Neurochir Suppl 2007; 97(1): 387-393.
6. Sheffler LR and Chae J. Neuromuscular electrical stimulation in neurorehabilitation.
Muscle Nerve 2007; 35:562-590.
7. Bogey R and Hornby TG. Gait training strategies utililzed in poststroke Rehabilitation:
are we really making a difference? Top Stroke Rehabil 2007; 14(60): 1-8.
8. Daly, JJ and Ruff RL. Construction of efficacious gait and upper limb functional
interventions based on brain plasticity evidence and model-based measures for stroke
patients. The Scientific World journal 2007: 7: 2031-2045.
9. Hara Y. Neurorehabilitation with new functional electrical stimulation for hemiparetic
upper extremity in stroke patients. J Nippon Med Sch 2008: 75: 3-14.
10. de Kroon JR, Ijzerman MJ, Chae J, Lankhorst GJ, Zilvold G. Relation between
stimulation characteristics and clinical outcome in studies using electrical stimulation to
improve motor control of the upper extremity in stroke. J Rehabil Med 2005; 37: 65-74.
11. Electrotherapy: Evidence-Based Practice. Sheila Kitchen and Sarah Bazin. Churchill
Livingston 2002, New York.
12. Baldwin ERL, Klakowicz PM, Collins DF. Wide-pulse-width, high frequency
neuromuscular stimulation: implications for functional electrical stimulation. J Appl
Physiol 2006;101:228-240.
13. Khaslavskaia s and Sinkjaer T. Motor cortex excitability following repetitive electrical
stimulation of the common peroneal nerve depends on the voluntary drove. Exp Brain
Res 2005; 162:497-502.
14. Evidence Based Review of Stroke Rehabilitation 10th edition. www.ebrsr.com.
15. Price CL, Pandyan AD. Electrical stimulation for preventing and treating post-stroke
shoulder pain: a systematic Cochrane review. Clin Rehabil 2001: Feb 15(1) 5-19.
Limitations
•Lack of adequately powered, well designed trials
•Insufficient current evidence for UK NICE approval, but recommended for ‘consideration’ in the UK RCP Stroke Guidelines
• All studies show wide variation in response - can we be more effective in targeting potentially ‘good responders’
•Meta-analysis is difficult because of different methodologies
Although there have been positive results with use of FES, to generalize and present a protocol for FES as a treatment is difficult. The problem lies with variability in methodology, limited random control studies, lack of standardized treatment protocols, variability in population utilized ( acute vs chronic).1,14 There is a definite need for large, multicentre, randomized clinical trials with defined population4 and evaluation of immediate and long term outcomes.6 It is difficult to determine exact parameters for electrical stimulation due to many confounding variables.10 There is further research required to examine and determine optimal dose and parameters.4,6 Techniques and systems need to be improved to encourage compliance.6 Lack of studies comparing FES with EMG triggered FES and neuroprostheses.6 Research has shown: FES can be used for the hemiparetic population that demonstrates limited residual movement.6 There does appear to be some limited evidence to support use of FES for shoulder pain and to decrease subluxation. Better outcomes with task specific activities than with generalized function.3,10 When using FES, repetition, novelty, active contribution 5,6,13 and function are key points for achieving motor relearning.6
There is a definite lack of large scale research to definitively support or dismiss the use of FES in treatment of hemiplegic limbs in stroke. There appears to be a push toward increased use of technology with robot arms and neuroprostheses as treatment adjuncts. The cost of this technology may prevent immediate access for clients in our health care system. Regardless, the emphasis is still on tapping into motor learning and neuroplasticity using techniques of repetition and task specific training to improve functional outcomes. Research does provide some support for utilizing FES in promoting motor relearning and with further refined research there will likely be the development of more definitive protocols for treatment.
Literature
Robbins SM, Houghton PE, Woodbury MG et al. (2006) The therapeutic effect of functional and transcutaneous electric stimulation on improving gait speed in stroke patients: a meta-analysis. Archives of Physical Medicine & Rehabilitation 87: 853–859.
Taylor PN, Burridge JH, Dunkerley AL et al. (1999) Clinical use of the Odstock dropped foot stimulator: its effect on the speed and effort of walking. Archives of Physical Medicine & Rehabilitation 80: 1577–1583.
Daly JJ, Roenigk K, Holcomb J et al. (2006) A randomized controlled trial of functional neuromuscular stimulation in chronic stroke subjects. Stroke 37: 172–178.
Kottink AI, Hermens HJ, Nene AV et al. (2007) A randomized controlled trial of an implantable 2-channel peroneal nerve stimulator on walking speed and activity in poststroke hemiplegia. Archives of Physical Medicine & Rehabilitation 88: 971–978.

## Slide 24
Self-directed arm therapy at home after stroke with a sensor-based virtual reality training system (nih.gov)

## Slide 25
0181-FI-cd.dvi (cereneo.ch)

## Slide 26
Hocoma | Webinar Sensor-based Technology Meets Physical Therapy

## Slide 27: Realidad virtual
4

## Slide 28: Evidencia clínica de la realidad virtual
Aspectos cognitivos
Ayuda en la rehabilitación cognitiva
Extremidad superior
Mejora la función de la extremidad superior y el procesamiento motor.
Entorno
Los entornos de VR estimulan los cambios neuroplásticos y mejora los efectos de aprendizaje.
Extremidad inferior
Mejora la velocidad de la marcha, velocidad y fuerza muscular mejorando con ello la calidad de vida general
(Rose et al. 1998)
(Rose et al. 1998)
(Kuttuva et al. 2006)
(Sviestrup 2004)
Motivación
Incrementa la autoconfianza y motivación
(Riva 1998)
Notes: Kuttuva, M, Boian, R, Merians, A, Burdea, G, Bouzit, M, Lewis, J, Fensterheim, D. The Rutgers Arm, a Rehabilitation System in Virtual Reality: A Pilot Study. Cyberpsych Behav., vol. 9, pp. 148-152, 2006.
Deutsch JE, Merians AS, Adamovich S, Poizner H, Burdea GC (2002) development and application of virtual reality technology to improve hand use and gait of individuals post-stroke. Restorative Neurology and Neuroscience, 20: 1-16
Reiss, T, Weghorst S. Augmented reality in the Treatment of Parkinson’s Disease. In Proceedings of Medicine Meets Virtual Reality 95; San Diego. IOS Press; 1995:298-302.
Riva, G. Virtual Reality in Paraplegia: A VR-Enhanced Orthopaedic Appliance for Walking and Rehabilitation. Stud Health Technol Inform., vol. 58, pp. 209-218, 1998.
Sviestrup, H. Motor Rehabilitation Using Virtual Reality. J. Neuroegr Rehab., vol. 1, pp.1-10, 2004.
  Individuals suffering from Parkinson’s disease have benefited from VR therapy through repetitive therapy of scrolling cues that aid their walking and help them work with the debilitating effects of akinesia (Reiss & Weghorst 1995)
  Individuals who suffer from hemiplegia as a result of a stroke are able to use virtual environments to improve their walking speed and muscle strength by increasing the symmetry of their walking, therefore improving their overall quality of life (Sviestrup 2004)
  Stroke patients have used VR in order to improve upper extremity function and motor processing (Kuttuva et al. 2006)
  Using VR during rehabilitation of spinal cord injured patients has helped to increase self confidence and motivation, therefore allowing the individual to rehabilitate in a more relaxed setting and increase the time he/she participates in activities. Spinal cord injured patients have learned to strengthen the muscles that they are able to control and maintain this strength in order to participate in everyday activities (Riva 1998)
  The high training effectiveness of VR in neurologicl and cognitive rehabilitation had been explained by “environmental enrichment” (Kolb 1999) that environmental effect was very important to patients’ recovery from brain injury. From animal studies, enriched VR environments might stimulate neuroplastic change in the cerebral cortex, enhance learning and problem-solving, and reduce cognitive impairment caused by brain damage (Rose et al. 1998)
Liepert J, Baunder H, Wolfgang HR, Miltner WH, Taub E, weiller C (2000) Treatment-induced cortical reorganization after stroke in humans. Stroke 31: 1210-1216
  Motivated patients would be encouraged to practice movements in a repetitive manner thereby improving their condition, an achievement that is not easy to attain via conventional therapy

## Slide 31
Hocoma | Webinar Virtual Rehabilitation - How Feedback and Motivation Influence Therapy Outcome

## Slide 32: Estimulación cerebral
5

## Slide 33: Evidencia clínica de la estimulacion cerebral
Dolor
Reduce entre un 20-58% el dolor crónico
Efecto óptimo
Las mayores ganancias se obtienen si se realiza con experiencias conductuales relevantes
Déficits graves
Mejoras incluso en pacientes con deficits motores graves
Función motora
Mejora de la función motora que puede durar varias semanas
(Fregni et al. 2006)
(Hummel et al. 2006, Boggio et al. 2006)
+
(Gladstone and Black 2000)
(Fregni et al. 2006)
Notes: rTMS seems to be effective, with mean pain relief in the range of 20–45% [25-27]. The outcome of rTMS is somewhat heterogeneous, however, as negative results have been reported [28].
only two studies have evaluated the effects of tDCS on chronic pain, they have shown even greater efficacy, with mean pain relief up to 58%. [29,30]
Stroke modulation
All of these studies showed a significant improvement in motor function when active stimulation was compared with sham stimulation. In addition, some of these studies showed that motor function improvement was associated with a change in neurophysiologic parameters. For instance, in three studies, motor function improvement was associated with an increase in cortical excitability in the affected hemisphere.59–61 Studies in which several sessions of noninvasive brain stimulation were administered showed that the effects could last for several weeks.59,62
even stroke patients with severe motor deficits seem to improve after appropriate stimulation of the lesioned or healthy primary motor cortex.63,64
Maximum behavioral gains with treatments that aim to modify cortical plasticity are found when such treatments are coupled with relevant behavioral experience.66,67
[25] Lefaucheur JP et al. (2004) Neurogenic pain relief by repetitive transcranial magnetic cortical stimulation depends on the origin and the site of pain. J Neurol Neurosurg Psychiatry 75: 612–616
[26] Pleger B et al. (2004) Repetitive transcranial magnetic stimulation of the motor cortex attenuates pain perception in complex regional pain syndrome type I. Neurosci Lett 356: 87–90
[27] Khedr EM et al. (2005) Longlasting antalgic effects of daily sessions of repetitive transcranial magnetic stimulation in central and peripheral neuropathic pain. J Neurol Neurosurg Psychiatry 76: 833–838
[28] André-Obadia N et al. (2006) Transcranial magnetic stimulation for pain control: double-blind study of different frequencies against placebo, and correlation with motor cortex stimulation efficacy. Clin Neurophysiol 117: 1536–1544
[29] Fregni F et al. (2006) A sham-controlled, phase II trial of transcranial direct current stimulation for the treatment of central pain in traumatic spinal cord injury. Pain 122: 197–209
[30] Fregni F et al. (2006) A randomized, sham-controlled, proof of principle study of transcranial direct current stimulation for the treatment of pain in fibromyalgia. Arthritis Rheum 54: 3988–3998.
[59] Fregni F et al. (2006) A sham-controlled trial of a 5-day course of repetitive transcranial magnetic stimulation of the unaffected hemisphere in stroke patients. Stroke 37: 2115–2122
[60] Kim YH et al. (2006) Repetitive transcranial magnetic stimulation-induced corticomotor excitability and associated motor skill acquisition in chronic stroke. Stroke 37: 1471–1476
[61] Hummel F et al. (2005) Effects of non-invasive cortical stimulation on skilled motor function in chronic stroke. Brain 128: 490–499
[62] Khedr EM et al. (2005) Therapeutic trial of repetitive transcranial magnetic stimulation after acute ischemic stroke. Neurology 65: 466–468

## Slide 36: Contacto
International Industry Society in Advanced Rehabilitation Technology (IISART)
General Information
info@iisartonline.org www.iisartonline.org
Centro Europeo de Neurociencias CEN
info@eneurocenter.com
www.eneurocenter.com

## Slide 37
Webinar: Breaking the Boundaries of Neurorehabilitation ENC - Hocoma

## Slide 38: Bibliografía
[1] Mehrholz et al. 2013, Electromechanical-assisted training for walking after stroke.
[2] Verbeek et al. 2014, What Is the Evidence for Physical Therapy Poststroke? A Systematic Review and Meta-Analysis.
[3] Mehrholz et al. 2012, Electromechanical and robot-assisted arm training for improving generic activities of daily living, arm function, and arm muscle strength after stroke.
[4] Sale et al. 2014, Effects of upper limb robot-assisted therapy on motor recovery in subacute stroke patients.
[5] Wagner et al. 2011, An economic analysis of robot-assisted therapy for long-term upper-limb impairment after stroke.
[6] Bartolo et al. 2014, Arm weight support training improves functional motor outcome and movement smoothness after stroke.
[7] Kloosterman et al. 2010, Influence of gravity compensation on kinematics and muscle activation patterns during reach and retrieval in subjects with cervical spinal cord injury: an explorative study.
[8] Krabben et al. 2012, Influence of gravity compensation training on synergistic movement patterns of the upper extremity after stroke, a pilot study.
[9] Prange et al. 2014, The effect of arm support combined with rehabilitation games on upper-extremity function in subacute stroke: a randomized controlled trial.
[10] Daly and Ruff 2007, Construction of efficacious gait and upper limb functional interventions based on brain plasticity evidence and model-based measures for stroke patients.
[11] Kottink et al. 2007, A randomized controlled trial of an implantable 2-channel peroneal nerve stimulator on walking speed and activity in poststroke hemiplegia.
[12] Hara 2008, Neurorehabilitation with new functional electrical stimulation for hemiparetic upper extremity in stroke patients.
[13] Ring and Weingarden 2007, Neuromodulation by functional electrical stimulation (FES) of limb paralysis after stroke.
[14] Arantes et al. 2007, Effects on Functional Electrical Stimulation applied to the wrist and finger muscles on hemiparetic subjects: a systematic review of the literature.
[15] Wilson et al. 2014, Peripheral nerve stimulation compared with usual care for pain relief of hemiplegic shoulder pain: a randomized controlled trial.
[16] Kuttuva et al. 2006, The Rutgers Arm, a Rehabilitation System in Virtual Reality: A Pilot Study.
[17] Sviestrup 2004, Motor Rehabilitation Using Virtual Reality.
[18] Rose et al. 1998, Virtual environments in brain damage rehabilitation: a rational from basic neuroscience.
[19] Riva 1998, Virtual reality in paraplegiga: a VR-enhanced orthopaedic appliance for walking and rehabilitation.
[20] Fregni et al. 2006, A sham-controlled, phase II trial of transcranial direct current stimulation for the treatment of central pain in traumatic spinal cord injury.
[21] Boggio et al. 2006, Hand function improvement with low-frequency repetitive transcranial magnetic stimulation of the unaffected hemisphere in a severe case of stroke.
[22] Gladstone and Black 2000, Enhancing recovery after stroke with noradrenergic pharmacotherapy: a new frontier?
[23] Fregni al. 2006, A randomized, sham-controlled, proof of principle study of transcranial direct current stimulation for the treatment of pain in fibromyalgia
[24] Hummel et al. 2006, Effects of brain polarization on reaction times and pinch force in chronic stroke.

## Slide 39: Fuente de las imágenes
Slide 2 – Audience Background: http://www.iisd.ca/ymb/climate/wcc3/pix/1sept/DSC_6266%20full%20room.jpg
Slide 3 – Reasons for New Technologies Left: http://www.unece.org/typo3temp/pics/8346dcaa95.jpg Middle (upper): http://emergingtech.tbr.edu/sites/default/files/styles/flexslider_full/public/NewTech_0.jpg?itok=WghHlgJO Middle (lower): http://timpexelectronics.com/wp-content/uploads/2014/03/Electronics-0000166421891-1100x732.jpg Right: http://www.nature.com/sc/journal/v41/n12/fig_tab/3101518f1.html
Slide 4 – Usage of New Technologies 1st image (motor learning): http://www.vi-hotels.com/typo3temp/pics/s_1ad5acb5b7.jpg 2ndimage (brain injury): http://www.eusi.org/wp-content/uploads/2012/11/stroke.jpg 3rd image (therapy): Hocoma 4th image (assessments): http://www.hopkinsmedicine.org/healthlibrary/GetImage.aspx?ImageId=268329 5th image (daily activities): http://static.guim.co.uk/sys-images/Guardian/Pix/pictures/2013/10/28/1382979259350/Gardening-and-DIY-can-pro-011.jpg
Slide 5 – Usage of New Technologies II Images: Presentation slides